## Slide 1: Gases, Clusters and Pellets: Jet Targets for Accelerator Experiments New Vistas in Low-Energy Precision Physics (LEPP) Kupferbergterrasse Mainz, April 4-7, 2016

## Slide 2: Typical Requirements on Internal Targets
Target material: H2, D2, N2, Ne, Ar,..., Xe
  Hydrogen as proton target for elementary reactions on the nucleon
  Deuterium as deuteron or effective neutron target
  Heavier gases (N2, Ne, Ar, ..., Xe) for interactions with large nuclei (high A, Z)
Pure target material without unwanted elements
  Windowsless, no target holder, ...
Pointlike interaction zone
Homogeneous spatial target density
Target thickness constant in time
  No time structures
  DAQ system ↔ dead time

## Slide 3: Typical Requirements on Internal Targets
Continously adjustable target thickness
  Optimum event rates for individual experimental situation
  Compensation of beam consumption → constant event rate
Target should be compatible with a close to 4p detector
The best target type depends on
  the experimental setup (detector, accelerator, DAQ, ...)
  the experimental program
  the required event rate (luminosity, cross section, ...)
Highly suited and well established:
Cluster targets, gas jet targets, pellet targets

## Slide 4: Production of Gas, Cluster and Pellet Beams

## Slide 5: Production of Gas, Cluster and Pellet Beams
dN/dm
100
1016
102
104
106
108
1010
1012
1014
Mass distribution

## Slide 7: Gas Jet Beams

## Slide 8: Production of Gas-Jet Beams
Expansion of gas through Laval nozzles into vacuum
Production of supersonic jets
High target thickness directly behind nozzle
  E.g. 1019 atoms/cm3
  Formation of typical node structure
But:
  Target thickness decreases rapidly with distance from nozzle
  Gas beam strongly expands in lateral direction
  High pumping speeds required

## Slide 9: Gas Jet Beams
Argon (293 K, 17 bar)
Nozzle: dmin = 0.5 mm
dout = 1.0 mm
dmin
dmax

## Slide 10: Gas Target Thickness Variation
Gas input pressure p0 variation
  target thickness changes within e.g. one order of magnitude
  thickness variation typically within seconds possible
Gas starting temperature T0 variation
  thickness changes within several orders of magnitude
  slow process (typically within minutes)

## Slide 11: Gas Target Thickness Variation
Hydrogen
Nozzle: dmin = 0.03 mm,
dmax = 3.5 mm
Numerical calculations:
Target thickness direcetly above nozzle exit
Hydrogen
Nozzle: dmin = 0.3 mm,
dmax = 3.5 mm
Argon
Nozzle: dmin = 0.5 mm,
dmax = 1.0 mm
O(1017) atoms/cm2
O(1019) atoms/cm2
O(1019) atoms/cm2

## Slide 12: Gas Flow and Vacuum Conditions
Target thicknesses and vacuum conditions, assuming a pumping speed of 1000 l/s in the nozzle chamber

## Slide 13: Gas Jet Beams
Argon (293 K, 17 bar)
Nozzle: dmin = 0.5 mm
dout = 1.0 mm
4 mm!

## Slide 14: Cluster Jet Beams

## Slide 15: Production of Cluster-Jet Beams
Expansion of croygenic gas/liquid through fine (e.g. Ø 30 µm) Laval nozzles
Condensation of gas or spraying of the liquid
  formation of nano- to micro-meter sized particles
  quasi-homogeneous beam

## Slide 16: Production of Cluster-Jet Beams
Target beam thickness strongly depends on
  nozzle properties (inner diameter e.g. 30 µm, shape, ...)
  gas/liquid input pressure p0
  gas/liquid input temperature T0
skimmer
p0/T0

## Slide 17: Production of Cluster-Jet Beams
Target beam thickness strongly depends on
  nozzle properties (inner diameter e.g. 30 µm, shape, ...)
  gas/liquid input pressure p0
  gas/liquid input temperature T0
skimmer
p0/T0
skimmer

## Slide 18: Production of Cluster-Jet Beams
Target beam thickness strongly depends on
  nozzle properties (inner diameter e.g. 30 µm, shape, ...)
  gas/liquid input pressure p0
  gas/liquid input temperature T0
skimmer
p0/T0
skimmer

## Slide 19: Production of Cluster-Jet Beams
Target beam thickness strongly depends on
  nozzle properties (inner diameter e.g. 30 µm, shape, ...)
  gas/liquid input pressure p0
  gas/liquid input temperature T0
skimmer
p0/T0
skimmer

## Slide 20: Production of Cluster-Jet Beams
Preparation of a cluster-jet beam by a set of two skimmers behind the nozzle
Constant opening angle of the cluster-jet after the second skimmer
cluster beam
second skimmer

## Slide 21: Cluster Beam Preparation by Skimmers
Skimmers (O(0.5 mm))
Cluster beam MCP images (after 5 m flight path)

## Slide 22: The PANDA Cluster-Source

## Slide 23: PANDA Cluster Target
PANDA cluster target + pumping system now fully in operation
Skimmer tip
cluster beam

## Slide 24: Planned PANDA Setup with Cluster Target

## Slide 25: Cluster Beam Profiles at the PANDA Vertex Point
T0=19 K
p0=18.5 bar
Well defined target beam at a distance of d = 2 m behind the nozzle (corresponds to PANDA interaction point)
Target thickness of 2x1015 H-atoms/cm3 achieved (2.1 m!)
x-direction
y-direction

## Slide 26: Target Thickness Variation
Gas/liquid input pressure p0 variation
  target thickness changes within one order of magnitude
  thickness variation typically within seconds possible
Gas/liquid starting temperature T0 variation
  thickness changes within several orders of magnitude
  slow process (typically within minutes)
p0=5-19 bar
T0=20-50 K

## Slide 27: Recent Results on Cluster Beams
Cluster masses as function of stagnation conditions (p0, T0) and nozzle diameter (dn) can be described well by Hagena law: Important for PANDA (event rate, DAQ, dead time, ...)
Esperanza Köhler, PhD thesis 2015
WWU Münster, Germany

## Slide 28: The Gas/Cluster-Jet Target for MAGIX
nozzle
Jet direction
For details see talk from
Silke Grieser (Wed.)

## Slide 29: Pellet Beams

## Slide 30: Production of Pellet beams
Injection of a jet of a cryogenic liquid through a thin nozzle into a gas close to triple-point conditions
Excitation of the nozzle by a piezoelectric transducer
→ periodic monosized droplets
Droplet size depends on nozzle diameter and piezo frequency
H2
He
He
pumping out
gas input
glass nozzle, Ø 10-20 µm

## Slide 31: Production of Pellet beams
Droplets pass through a thin tube into vacuum („vacuum injection“)
→ cooling due to surface evaporation
→ frozen pellets
Pellets pass the scattering chamber
glass nozzle
hydrogen droplets
Ø ~ 10 µm
f = 181 kHz

## Slide 32: Prototype for PANDA: The Jülich/Moscow Target
1 cm
condenser
triple point
chamber
glass sluice
generator

## Slide 33: A Pellet Target in Operation: WASA-at-COSY
glass nozzle
vacuum injection
droplets
skimmer
pellets
vacuum injection
droplets
skimmer
pellets

## Slide 34: A Pellet Target in Operation: WASA-at-COSY
glass nozzle
vacuum injection
droplets
skimmer
pellets
vacuum injection
droplets
skimmer
pellets

## Slide 35: Pellet Tracking System
Determination of the velocity and 3D-vertex information of individual pellets by a multi-camera tracking system
Aimed resolution: < 1mm
Upper tracking device with two
levels close to the pellet
generator (8 linescan cameras)
Lower tracking device with two
levels at the beam dump
(8 linescan cameras)
B
A
time difference

## Slide 36: Summary
Gas jet beams:
  All types of gases can be used
  High target beam thickness (e.g. O(1019) atoms/cm3) directly behind the nozzle
  Interaction point very close to the nozzle
  High gas load at the interaction point
  Rapid expansion of the beam in all directions
  Target beam without time structure
  Simple target thickness variation
  Compact target beam generator possible

## Slide 37: Summary
Cluster jet beams:
  All types of gases can be used
  High target thickness (e.g. O(1019) at./cm3) close to nozzle
  High target beam thickness (O(1015) at./cm3) also at large distances from the nozzle, i.e. 2 m
  Target generator can work as gas and/or cluster source
  Interaction point very close to nozzle or at larger distances
  Easy target beam shaping and lower gas load at the interaction point by use of specially shaped collimators
  Well defined beam shape even at large distances
  Target beam with (nearly) no time structure
  Simple target thickness variation
  Compact target beam generator possible

## Slide 38: Summary
Pellet beams:
  All types of gases can be used
  Pellets with uniform size/diameter
  Individual pellets (Ø 20 µm) have a mean thickness of O(1019) atoms/cm2
  Effective target beam thickness of e.g. O(1015) atoms/cm2 at large distances from the nozzle, i.e. 2 m
  Target beam shaping and lower gas load at the interaction point by use of collimators
  Well defined beam shape even at large distances
  Target beam with time structure
  Target thickness variation possible (time structure)
  More complex and larger target generator size

## Slide 39
Thank you very much....

## Slide 41: First Cluster Beams (03.12.2015!)
skimmer
Cluster beam
Skimmer tip
T = 22 K, p = 17 bar
T = 22 K, p = 16 bar

## Slide 42: Mechanical Adjustments
Both skimmers can be moved during operation
  Alignment of the target beam in the scattering chamber
The complete nozzle setup can be tilted relative to the (fixed) skimmer
  Selection of the high-density cluster core
skimmer
skimmer
nozzle (not visible)
skimmer

## Slide 43: Mechanical Adjustments

## Slide 44: Recent Results on Cluster Beams
Studies on cluster mass distributions (here: hydrogen in gaseous phase before entering the nozzle)
Cluster beam mass distribution can be described well by log-normal distribution
Esperanza Köhler, PhD thesis 2015

## Slide 45: From the Prototype to PANDA
Optimization and design studies on the pellet generator in progress (ITEP)
Design of the pellet tracking is fixed and will be build up and optimized
(Univ. Uppsala)

## Slide 46: Expected Target Parameters at PANDA
 | Cluster Target | Pellet Target | 
 |  | PTR mode (tracking) | PHL mode (high luminosity)
Effective target thickness | > 1x1015 at./cm2 | ≤ 2x1015 at./cm2 | ≥ 4x1015 at./cm2
Cluster/Pellet size | nm - µm | Ø ≥ 20 µm | Ø ≤ 15 µm
Cluster/Pellet frequency | Continuous beam | ≈ 15 k plt/s | ≥ 150 k plt/s
Target stream diameter | 4 mm x 12 mm | Ø ≈ 3 mm | Ø ≤ 3 mm
Average dist.between cluster/pellets | ≤ 10 µm | ≥ 4 mm | << 4 mm
p beam size | Ø ≤ 1 mm | Øvertical ≥ 3.5 mm | Øvertical ≤ 3.5 mm
Average no. of cluster/pellets in p beam | ≥ 107 | ≈ 1 | ≈ 10