## Slide 1: Bachelor- und Masterarbeit The Gas Electron Multiplier - Recent Developments and Applications
Bernhard Ketzer
Helmholtz-Institut für Strahlen- und Kernphysik
Universität Bonn

## Slide 2: Limitations of Wire-based Detectors
Localization accuracy: typ. 100-500 mm
Volume / 2-track resolution: typ. 10×10×10 mm3 (signal induction on pads)
Rate capability: limited by build-up of positive space-charge around anode
[A. Breskin et al., NIM 124, 189 (1974)]
e-
~ 100 ns
I+
~ 100 µs

## Slide 3: Limitations of Wire-based Detectors
Localization accuracy: typ. 100-500 mm
Volume / 2-track resolution: typ. 10×10×10 mm3 (signal induction on pads)
Rate capability: limited by build-up of positive space-charge around anode
Ion backflow: IB = Icathode / Ianode ~ 30% for TPC with MWPC
e-
~ 100 ns
I+
~ 100 µs

## Slide 4: Limitations of Wire-based Detectors
Localization accuracy: typ. 100-500 mm
Volume / 2-track resolution: typ. 10×10×10 mm3 (signal induction on pads)
Rate capability: limited by build-up of positive space-charge around anode
Ion backflow: IB = Icathode / Ianode ~ 30% for TPC with MWPC
Aging and discharge damage: polymerization of organic compounds
Reduction of cell size
by a factor of 10
Photolithography
Etching
Coating
Wafer post-processing
[O. Ullaland, LBL-21170, 107 (1986)]

## Slide 5: The MPGD Zoo
Microdot Chamber
[S.F. Biagi et al., NIM A361, 72 (1995)]
Microgap Chamber (MGC)
[F. Angelini et al., NIM A335, 69 (1993)]
Micro Wire Detector
[B. Adeva et al., NIM A435, 402 (1999)]
Compteur à Trous (CAT)
[F. Bartol et al., J. Phys. III 6, 337 (1996)]
WELL Detector (mCAT)
[R. Bellazzini et al., NIM A423, 125 (1999)]
50 mm
Micro Groove Counter
[Bellazzini et al., NIM A424, 444 (1999)]
and many more...
Microstrip Gas Chamber
[A. Oed, NIM A263, 351 (1988)]
10 mm
80 mm

## Slide 6: GEM
70 mm
GEM: Gas Electron Multiplier
[F. Sauli, NIM A386, 531 (1997)]
Thin polyimide foil, typ. 50 mm
Cu-clad on both sides, typ. 5 mm
Photolithography: ~ 104 holes/cm2
Granularity 10×higher than MWPC
DU=300-500 V
   high E-field: ~50 kV/cm
   avalanche multiplication

## Slide 7: GEM
higher gain at lower GEM voltages
[S. Bachmann, B. Ketzer et al., NIM A479, 294 (2001)]
discharge prevention
[B. Ketzer et al., IEEE Trans. Nucl. Sci. 48, 1065 (2001)]
no aging up to 7 mC/mm2
[C. Altunbas, B. Ketzer et al., NIM A515, 249 (2003)]
Triple GEM amplification
GEM: Gas Electron Multiplier
[F. Sauli, NIM A386, 531 (1997)]
Thin polyimide foil, typ. 50 mm
Cu-clad on both sides, typ. 5 mm
Photolithography: ~ 104 holes/cm2
Granularity 10×higher than MWPC

## Slide 8: MPGD in Running Experiments
Exp. | # | Type | Readout | # of ch. | Size (cm2) | Gas | sspace (mm) | stime (ns) | e (%)
COMPASS | 22 | GEM | 2-D strips | 1536 | 31×31 | Ar/CO2 (70/30) | 70 | 12 | >97
 | 12 | MM | 1-D strips | 1024 | 40×40 | Ne/C2H6/CF4 (80/10/10) | 90 | 9 | >97
LHCb | 24 | GEM | pads | 192 | 10×24 | Ar/CO2/CF4 (45/15/40) |  | 4.5 | >97
TOTEM | 40 | GEM | pads + strips | 1536 + 256 | 30 × 20 | Ar/CO2 (70/30) | ~70 (q) |  | >92
30 cm
also CAST, NA48, PHENIX …

## Slide 9: New Challenges
Special shapes
  cylindrical
  spherical
Higher rates
Pixel readout
Ion backflow suppression
Larger active areas
  Bulk Micromegas
  Single-mask GEMs
Aging, discharge protection
  Materials
  Multi-stage amplification
  Segmentation
  Resistive coating
Higher resolutions
  mPixel
  InGrid

## Slide 10: GEM Manufacturing
Limitations of double-mask technique
1. Image transfer using two film
masks (photoplotted polyester)
 Difficult above 400×400 mm2
due to
  Film accuracy
  Temperature and humidity variations
  Alignment of masks
2. Raw material:
  rolls of 100 m × 0.457 m
  new: 0.6 m width
Notes: Raw material: APICAL + vacuum deposited Cu (no glue)
Cu etching: FeCl3 + HCl
Kapton etching: Ethylenediamine (C2H8N2) + KOH + Ethanol

## Slide 11: Single-Mask Process
Photoresist deposition on base material
Photoresist hole patterning (single mask)
15um resist
15um resist
Top copper etching
Resist stripping
Polyimide anisotropic etching
Bottom resist protection deposition
Bottom copper etching
Top copper protected by galvanic connection
Resist stripping
Soft polyimide etching
[M. Villa et al., arXiv 1007.1131v1]
Notes: Top cover protection:
3 V DC to to top electrode
GND on basin walls
-> DC current from wall to top electrode, making it inert to the etching bath.

## Slide 12: CMS Muon Chambers
CMS Muon Detector Upgrade: REi/1
[M. Tytgat, MPGD 2013]
990 x (220-455) mm2
Radial Readout Strips
0.6 to 1.2 mm pitch

## Slide 13: CMS Muon Chambers
990 mm
TRIPLE GEM
~ 260 µm
D. Abbaneo et al, JINST 9(2014)C01053
EFFICIENCY
POSITION ACCURACY

## Slide 14: New Challenges
Special shapes
  cylindrical
  spherical
Higher rates
Pixel readout
Ion backflow suppression
Larger active areas
  Bulk Micromegas
  Single-mask GEMs
Aging, discharge protection
  Materials
  Multi-stage amplification
  Segmentation
  Resistive coating
Higher resolutions
  mPixel
  InGrid

## Slide 15: COMPASS PixelGEM
Pixel + strip readout
Center: 32×32 pixels, 1 mm2
Periphery: 2×512 strips (2D)
Readout electronics moved
away from the beam
450 mm

## Slide 16: COMPASS GEM Detectors
31 cm
2-D Strip readout: 22 detectors
Thickness: 0.4% X0
Resolution: sx=70mm, st=12ns
Pixel + Strip readout: 5 detectors
Thickness: 0.26% X0
Resolution: sx=125mm, st=11ns
High rates: ~105 mm-2s-1
Large-area GEM
PixelGEM
[B. Ketzer et al., NIM A535, 314 (2004)
B. Ketzer et al., IEEE NSS 2007, N12-5 (2007)]

## Slide 17: New Challenges
Special shapes
  cylindrical
  spherical
Higher rates
Pixel readout
Ion backflow suppression
Larger active areas
  Bulk Micromegas
  Single-mask GEMs
Aging, discharge protection
  Materials
  Multi-stage amplification
  Segmentation
  Resistive coating
Higher resolutions
  mPixel
  InGrid

## Slide 18: Time Projection Chamber
An (almost) ideal tracking detector:
Large acceptance
Large active volume
Low material budget
3D picture of event
   simple pattern recognition
Extremely high particle densities
 heavy ion experiments
Good momentum resolution
Particle identification
Examples:
STAR (420 cm × 400 cm)
ALICE (500 cm × 500 cm)
Limitations:
No redundancy
Calibration very demanding
Drift distortions due to ion backflow
Gating  low trigger rates
Notes: In the last 3 years, ALICE has delivered a wealth of new data on heavy ion collisions at unprecedented energies to study the properties of the QGP

## Slide 19: Time Projection Chamber
Examples:
STAR (420 cm × 400 cm)
ALICE (500 cm × 500 cm)
Limitations:
No redundancy
Calibration very demanding
Drift distortions due to ion backflow
Gating  low trigger rates

## Slide 20: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events

## Slide 21: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events

## Slide 22: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events

## Slide 23: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events

## Slide 24: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events

## Slide 25: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events

## Slide 26: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events

## Slide 27: Operation at High Rates
High rates: drift time > 1 / (event rate)  overlapping events
Goal: operate TPC continuously
  analog event pipeline
  3D “Movie”
ALICE: Operate at high luminosity
       Record all minimum bias events
       50 kHz in Pb-Pb collisions, i.e. 100× higher than present

## Slide 28: Ion Backflow Suppression in GEM
Low ion density in drift region requires
  low primary ionization
  low gain
  low ion backflow

## Slide 29: FOPI GEM-TPC
Light-weight field cage
Drift length 725 mm
Ø 105-300 mm
Triple GEM amplification
10254 ch., AFTER ASIC
Gas: Ar (Ne)/CO2 (90/10)
[B. Ketzer et al., NIM A 732, 237 (2013),
M. Ball et al., arXiv1207.0013, 2012]
Notes: Very thin FC walls: 4mm Kapton/Rohacell sandwich

## Slide 30: dE/dx Resolution
Gain equalisation using 83mKr:
  Main peak 5.1%
PID using dE/dx:
  Resolution ~ 18%
  in agreement with expectation
  no density correction yet
First dE/dx measurement
with GEM-TPC
[F.V. Böhmer et al., NIM A 737, 214 (2014)]

## Slide 31: ALICE: The Space Charge Challenge
Ion blocking in GEMs not as efficient as with gating grid
ALICE Goal: IB = 1%, e = 20 at G = 2000
ions from 8000 events in drift volume!
Distortions up to 19 cm in and 7 cm in (near drift cathode for small radii)
Well below 10 cm for the largest part of drift volume
Similar to STAR TPC at RHIC
to be corrected to the level of intrinsic resolution!

## Slide 32: Ion Backflow – Rate Dependence
Ar/CO2 (70/30)
Poisson equation:
For homogenous space charge density and parallel plate boundary conditions:
d
drift
z
Expected after LS2: 5000 fC/cm2

## Slide 33: Charge Transfer in Single GEM
similarly for back-drifting ions…
Need to understand charge transfer  simulations + measurements

## Slide 34: Ion Backflow
But: very little diffusion for ions
   beware of hole alignment: critical for IB!
Deliberate misalignment of holes difficult
Rotate foils by 90° to avoid long-range variations: Moiré pattern

## Slide 35: Charging-Up of GEM Foils
Observed experimentally: initial increase of gain under irradiation
Generally ignored in simulations!
Attempt to study the effect in simulations:
  Calculate electric field
  Simulate gas avalanches
  Record charges ending up on insulator
  Add corresponding charge to electric field calculation
Result:
  Charge on insulator reduces losses
  Saturation reached after 3·106 eprim/hole
  Gain increases by ~30%

## Slide 36: Ion Backflow – ALICE Solution
Triple-GEM setup not sufficient
New chambers: 4-GEM setup with standard (S) and large pitch (LP)
Field configuration optimized to provide
    IB < 1%
    sE/E < 12% (for 55Fe X-rays)
    Discharge stability
Standard pitch
Large pitch
140 mm
280 mm

## Slide 37: Ion Backflow – ALICE Solution
Triple-GEM setup not sufficient
New chambers: 4-GEM setup with standard (S) and large pitch (LP)
Field configuration optimized to provide
    IB < 1%
    sE/E < 12% (for 55Fe X-rays)
    Discharge stability
Ion blocking:
GEM1: asymmetric field
GEM2/GEM3: geometric blocking
GEM4: asymmetric field

## Slide 38: Charge Transfer in 4-GEM System
Simulation of charge transfer for 4-GEM system:
GEM1 (S)
GEM2 (LP)
GEM3 (LP)
GEM4 (S)
collection efficiency
extraction efficiency
absolute gain
effective gain
number of produced e-ion pairs
number of ions drifting back into
drift volume

## Slide 39: IB vs Energy Resolution
IB and energy resolution are anticorrelated when UGEM1 is varied
Goals have been reached, even with some margin for fine-tuning
Much larger phase space scanned  no significant improvement expected

## Slide 40: ALICE TPC Upgrade

## Slide 41: ALICE TPC Upgrade
50cm
114cm
47cm
87cm
Notes: Detector to be operated in a completely new environment
single-mask technology
4-GEM stack
S-LP-LP-S

## Slide 42: ALICE TPC Upgrade

## Slide 43: Front-end Electronics
SAMPA ASIC:
Polarity opposite wrt MWPC
Continuous readout  simultaneous sampling and data transfer
Data throughput: (of FEE, not written to disk)
Triggered mode for calibration
Digital filter for common mode correction in DSP

## Slide 44: New Challenges
Special shapes
  cylindrical
  spherical
Higher rates
Pixel readout
Ion backflow suppression
Larger active areas
  Bulk Micromegas
  Single-mask GEMs
Aging, discharge protection
  Materials
  Multi-stage amplification
  Segmentation
  Resistive coating
Higher resolutions
  mPixel
  InGrid

## Slide 45: KLOE-2 at DAFNE
DC wall
New inner tracker:
Reconstruction of KS and h,h’ decays
srf~200 mm, sz~500 mm
Extremely light-weight: < 2% X0
5 kHz/cm2 rate capability
Luminosity upgrade: 5 – 10 fb-1/yr
DAFNE: e+e-F, √s~mF=1.02 GeV
[KLOE-2 Inner Tracker TDR , arXiv:1002.2572]

## Slide 46: C-GEM for KLOE-2
DC wall
5 cylindrical triple GEM detectors:
no spacers
Ø=260 - 460 mm, L=700 mm
stretched at end caps
XV stereo strip readout (40°)
Pitch 650 mm

## Slide 47: C-GEM for KLOE-2
KLOE-2 Inner Tracker: Three layers of Triple-GEM detectors
A. Balla et al, Nucl. Instr. and Meth. A732(2013)221
SPATIAL RESOLUTION
(X: Bending Plane):

## Slide 48: Spherical GEM
Elliminates parallax error
X-ray diffraction
Neutrons, photon
Thermoplastic heat forming
[S. Duarte Pinto et al., IEEE NSS Conference Record N11-1, 2009]

## Slide 49: Conclusions
MPGD (GEM, MM) have matured to reliable detectors
Overcome drawbacks of wire-based detectors:
  rate capability, resolution, ion backflow,
  radiation hard
Big progress in last 5 years:
  large active areas: CMS, ATLAS, ALICE, Kloe-2 (cylindrical)
  microscopic understanding improved: charging-up, charge transfer
  discharge stability: multi-GEM, resistive coating
TPC with GEM allows for continuous readout  3D movie
What I did not cover:
new materials and geometries: THGEM, Glass, Ceramic, Graphene, …
mPixel readout, InGrid
photon detection
dual-phase TPC, electroluminescence, TPC-RICH, active-target TPC

## Slide 50: Conclusions
MPGD: reliable detectors
Good resolution: t, x, E
High rate capability
Radiation hard
Ion backflow reduction
Photon feedback reduction
Inexpensive
Large active areas

## Slide 51: Outlook
RD51 (CERN):
~73 institutes worldwide
430 authors
Work packages
Test beam facility
http://rd51-public.web.cern.ch
Future Experiments:
STAR
ATLAS, CMS (muon)
ALICE, COMPASS (RICH)
TOTEM (T1)
PANDA, CBM
ILC (TPC, DHCAL)
JLAB
- Inner Tracker & Vertex: gas
TPC: gas
Outer Tracker: gas
Calorimeters in outer region

## Slide 52: Spare Slides

## Slide 53: Electric Fields

## Slide 54: GEM Manufacturing
50 mm Kapton
5 mm Cu both sides
Photoresist coating,
masking and
exposure to UV light
Metal chemical etching
Kapton chemical etching
Second masking
Metal etching,
cleaning, passivation
Notes: Raw material: APICAL + vacuum deposited Cu (no glue)
Cu etching: FeCl3 + HCl
Kapton etching: Ethylendiamine (C2H8N2) + KOH

## Slide 55: GEM Manufacturing
50 mm Kapton
5 mm Cu both sides
Photoresist coating,
masking and
exposure to UV light
Metal chemical etching
Kapton chemical etching
Second masking
Metal etching,
cleaning, passivation
70 µm
55 µm
5 µm
Standard GEM:70 µm Ø at 140 µm pitch
Notes: Raw material: APICAL + vacuum deposited Cu (no glue)
Cu etching: FeCl3 + HCl
Kapton etching: Ethylendiamine (C2H8N2) + KOH

## Slide 56: PixelGEM Readout Plane
Pixel plane: 2 layers (50mm)
Strip plane: 2 layers (50mm)

## Slide 57: Readout Plane
x strips
y strips
pixels

## Slide 58: COMPASS PixelGEM
sx=135mm
st=7.3ns
High intensity muon beam: up to 1.2·105 /mm2/s
[B. Ketzer et al., IEEE NSS Conference Record N12-5, 2007]
[A. Austregesilo et al., Nucl.Phys.Proc.Suppl.197:113-116,2009]

## Slide 59: CMS Muon Chambers
Present Muon System:
  Drift Tubes
  Cathode Strip Chambers
  RPC
  no coverage for |h|>1.6
  (REi/1)
Proposal:
triple GEM
990 × (220 - 455) mm2
[D. Abbaneo et al., RD51-Note-2010-005-1]
S-LHC: Requirements for REi/1 locations:
  L~1034-35 cm-2 s-1
  Flux: several 10 kHz/cm2
  Total integrated charge: several 10 C/cm2
  Triggering capability

## Slide 60: Performance of Single-Mask GEMs
Gain compatible with double-mask GEMs
Charging-up time seems to be slightly shorter
[M. Villa et al., arXiv 1007.1131v1]

## Slide 61: The ALICE Detector
Volume: ~ 90m3
Gas: Ne/CO2(/N2) (90/10/5)
Drift voltage: 100kV, 94ms drift time
72 MWPCs with 557768 readout pads
Main tracking device: TPC
at 10 GeV
-0.9 < h < 0.9
(159 clusters)
Readout rate: 500 Hz (Pb-Pb)

## Slide 62: Discharge Studies

## Slide 63: Quality Assurance
QA protocol has been developed:
HV „cleaning“ of foils to remove residual dust (production, transport)
Electrical characterization: leakage current, discharges (in dry gas!))
Precision optical scanning: defects, distribution of hole diameters
Gain mapping

## Slide 64: Influence of Humidity
Mean and variance of Ileak (excluding ramping) for every sector
Strong dependence on humidity, often non-reproducible
Slightly lower currents after additional HV cleaning
Number of discharges increasing with humidity

## Slide 65: Baseline Shift at High Rates
Strong capacitive coupling between anode pads due to GEM foil above
Consequence: common mode signal due to charges arriving on full pad plane
ALICE:
Conventional filter: moving average
  unstable: may fail
New non-linear filter: slope-based
  reliably follows baseline
Implemented on DSP of SAMPA chip

## Slide 66: Reconstruction Strategy
Two-stage reconstruction scheme:
Cluster finding, cluster-to-track association: 5 TB/s  50 GB/s
  Scaled average space charge distortion map, , gain eq. 
Tracking, ITS-TRD track matching
  High-resolution space charge correction  in

## Slide 67: Reconstruction Strategy
Notes: Figure 7.17 shows the ITS-TPC matching effiency (left) as well as the transverse momentum resolution
(right) obtained from a full MC, implementing the remaining residual space charge distortions after
applying the calibration procedure described in Sec. 8.4.
The matching efficiency is above 95% for all momenta. For standalone TPC tracks (red), the pT resolution is slightly worse than the one obtained without distortions (see also Fig. 7.6), while for TPC tracks constrained to the interaction vertex (blue) and tracks matched to the ITS (black) the performance is practically the same as for the ideal case without space-charge distortions

## Slide 68: Neutron Detection with GEM
Coating of GEMs with 1-3 mm 10B
10B+ng7Li+a
Stack of 8 coated GEM foils
efficiency 23% at 2.5Å
Rate capability > 2.7 MHz/cm2
Time resolution < 1ms
Spatial resolution 4mm
CASCADE
[http://www.physi.uni-heidelberg.de/physi/cascade/]

## Slide 69: Cobra
reached
problem of IB completely eliminated!
to be studied: e- transparency, size
[A. Lyashenko et al., NIM A 598 (2009) 116–120]

## Slide 70: New Challenges
Special shapes
  cylindrical
  spherical
Higher rates
Pixel readout
Ion backflow suppression
Larger active areas
  Bulk Micromegas
  Single-mask GEMs
Aging, discharge protection
  Materials
  Multi-stage amplification
  Segmentation
  Resistive coating
Higher resolutions
  mPixel
  GridPix

## Slide 71: MPGD readout by Pixel ASIC
Ultimate resolution:
Only diffusion-limited
Granularity = primary ionization
cluster spread: pixel size < 100mm
`Naked’ CMOS pixel chip:
charge collecting pad
preamplifier, shaper
discriminator / sample&hold
data readout (MUX)
CMOS ASIC: 2100 pixels, 80mm
[R. Bellazzini et al., NIM A535, 477 (2004)]
MediPix2 / TimePix: 65k pixels, 55mm
[X. Llopart et al., TNS 49, 2279 (2002)]
Resolve individual clusters!
pattern recognition & track
fitting in dense environment
dE/dx resolution for TPC

## Slide 72: The Electronic Bubble Chamber
14 mm
Setup:
Triple GEM
He/CO2 or Ar/CO2
TimePix
TOT + Time info
[A. Bamberger, NIMA 573, 361 (2007)]

## Slide 73: InGrid
Deposit anode
UV exposure
Deposit metal
Pattern metal
Develop resist
Deposit SU-8
photoresist
Insulating
pillars
Integrated Micromegas and Pixel Sensor
(Si wafer post-processing & MEMS)
[J. Timmermans, VCI 2007]
Notes: MEMS: Micro electro-mechanical systems
holes aligned to readout pads
support pillars in between

## Slide 74: Discharge Protection
Deposit of resistive layer on pixels
Double amplification
 local reduction of E field
20 mm a-Si, r=2 108 W cm
7 mm Si3N4, r=108-1015 W cm
SiNProt
Notes: Discharges:
evaporation of surface structure of chip due to hot plasma
too large input charge damaging the pixel circuitry

## Slide 75: InGrid TPC for ILD

## Slide 76: GridPix
Drift gap ~ 10-20 mm
Recording of arrival time  3D track image
Small drift distance  minimize diffusion
Small capacitive load: < 10 fF
No leakage currents
 low noise: < 100 e-

## Slide 77: Gossip
Reduced drift gap: 1 – 1.2 mm
 collection of e- within 25 ns
No radiation damage of detection
medium (gas is exchanged)
Small amount of material
Probability for d-e- small
Low sensitivity to neutrons and X-rays
Proposal for Gaseous Pixel Detectors
for the ATLAS Inner tracker at the sLHC
[H. van der Graaf, F. Hartjes, A.-P. Colijn, ATL-P-MN-0016]
Gas on Slimmed Silicon Pixels

## Slide 78: Photon Detection with THGEM

## Slide 79: Graphene on GEM

## Slide 80: TPC-RICH for sPHENIC, EIC
[C. Woody et al.]

## Slide 81: Dual-phase TPC