## Slide 1: FOOT FragmentatiOn Of Target
55th International Winter Meeting on Nuclear Physics
Bormio 23-27 January 2017
An experiment for the measurement of nuclear fragmentation cross sections for Particle Therapy
G. Battistoni (INFN, Milano)
for the FOOT Collaboration

## Slide 2: Rationale of Charged Particle Therapy
Radiotherapy concerns ~50% of all cancer patients. ~ 2M patients/year.
“Conventional” radiotherapy (photons)
Charged (hadron) particle therapy
mostly protons;
in few cases 12C beams
Advantageous for some kind of pathologies
Peak of dose released at the end of the track, better sparing the normal tissue
Beam penetration in tissue function of the beam energy
Accurate conformal dose to tumor with Spread Out Bragg Peak
Nuclear physics is contributing to the development of hadrontherapy: Accelerator technology, Detectors, Monte Carlo codes and other software, study of contribution of nuclear reactions, ...

## Slide 3: Typical example of advantages of Charged Particle Therapy
35% local recurrence
Preventable distant metastases
Large volumes irradiated
Early, late and very late normal tissue damage
Image guided, conformal (IMRT), photon therapy
Conformal Proton therapy: higher selectivity!
The future development of Charged Particle Therapy is strongly related to the possibility of demonstrating the effective reduction of complication probability in normal tissues for the same (or sometimes better) control of the tumoral region

## Slide 4: The concept of RBE
D0
SFXR
SFp
1 10 100 LET (keV/μm)
RBE
4
3
2
1
for a given type of biological end-point and its level of expression.
For example: Survival Fraction 10%
Protons: RBE slowly varying with LET, approximated by a constant 1.1 factor (➞ 10% more effective than photons)
Ions with Z>1 can have ΡRΒΕ significantly >1

## Slide 5: Protons are not simply like Photons*1.1
New Paradigm for Proton Radiobiology
(Girdhani 2013 Radiat Res)
Resulτs point out that Protons and photons present distinct physics and biological properties at Sub-Cellular, Cellular and Tissue level
Do nuclear interaction play a role?
It has been pointed out a possible impact of variable proton RBE on Normal Tissue Complication Prob. values. Present Treatment Planning does not take this into account
Paganetti 2002 PMB
Εxperimental determinations of RBE exhibit large fluctuations. RBE could be significantly >1.1
RBE=1.1
Variable RBE

## Slide 6: The two sides of the problem
Exp. Data (points) from Haettner et al, Rad. Prot. Dos. 2006
Simulation: A. Mairani PhD Thesis, 2007, Nuovo Cimento C, 31, 2008
A) Ion Therapy:
Known effect of Nuclear Fragmentation of Projectile:
mixed contribution of different RBE/LET
Considered in treatment, but still scarce validation data!
B) Proton Therapy:
Nuclear Fragmentation of Target
Possible contribution to biological effect
Not considererd in treatment plannig so far
Data exisiting only for production
of very light fragments (nucleons)
Bragg peak in a water phantom
400 MeV/u C beam
New

## Slide 7: Target fragmentation & healthy tissue
Target fragmentation in proton therapy gives higher contribution in healthy tissue, where beam is still energetic (~200MeV) !!
About 10% of biological effect in the entrance channel due to secondary fragments (Grun 2013)
Largest contributions of recoil fragments expected from
He, C, Be, O, N
In particular on
Normal Tissue Complication Probability
See also :
- Paganetti 2002 PMB
- Grassberger 2011 PMB
200 MeV proton beam in water
R=1/8
R=1/40
Cell killed by ionization
Recoil fragment generated
7
Cancers 2015,7 Tommasino & Durante

## Slide 8: p+C, p+O scattering @200 MeV
The elastic interaction and the forward Z=1,2 fragment production are quite well known. Uncertainties on large angle Z=1,2 fragments.
Missing data on heavy fragments.
Very low energy-short range fragments, almost isotropic.
MCs confirm this picture but…..
Nuclear model & MC not yet reliable or benchmarked at the needed level
Needed Z>2 fragment yields and emission energy
O
C
H
FLUKA MC:
16O beam 200 MeV/u on C2H4 target
For Z>3 everything is within 10 MeV/u
The range can be as low as tens of micron!!

## Slide 9: An example of target fragmentation at work: BNCT

## Slide 10: Inverse kinematic strategy
Shooting a proton (for instance Ekin=200 MeV  β~0.6) on a “patient” (i.e. at 98% a C,O,H nucleus) could not be the right choice. In particular large systematic on the fragment yields and energies can be due to the non zero target thickness.
A possible work around is to shoot a β=0.6 patient ( i.e. O,C beam) on a target made of protons and measure the fragments..
Use as beams the ions that are the constituents of the patient (mainly 16O, 12C) with Ekin/nucl ~ 200MeV/u.
Use twin targets made of C and polyethylene (C2H4)n and obtain the fragmentation results on H target from the difference
Apply the reverse boost with the well known β of the beam
CAVEAT!: The fragment direction must be well measured in the Lab frame to obtain the correct energy in the patient frame

## Slide 11: Experience at GANIL

## Slide 12: Monte Carlo Predictions: example
Direct kinematics: 16O beam 200 MeV/u on C2H4 target
FLUKA MC code
Fragment production spectra
Normalized at the same peak value

## Slide 13: Radiobiology requests & detector constraints
Heavy fragment (Z>2) production cross section with uncertainty of 5%
Fragment energy spectrum (i.e. dσ/dE) with 1-2 MeV/u accuracy
Capability of resolving Z of fragment
Capability of resolving isotopes, at least for lower Z nuclei.
Study light ions production at large angle
Angular resolution in “patient frame” is instead not relevant. Fragments have a very short range
To implement sound NTCP models the requirements on the knowledge of the p+C,O interaction @200 MeV are very strict:

## Slide 14: Guide lines for the detector
Main focus on Z>2 fragment yields & emission energy. Precise angle measurement are also needed to apply correct inverse boost transformation
The fragment charge ID is the basis of the measurement.
The fragment mass ID is a challenge and can be performed after a Z ID. An eventual wrong A assignment has an effect on the range evaluation-> less severe at high A
PID achieved due to combinaton of measurements of energy, momentum and TOF measurement of fragments
The fragmentation contribution due to detector material MUST be kept as low as possible and eventually subtracted
Detector portability to different beams is an absolute need: size of the detector should be in the 2 meters range

## Slide 15: The FOOT Detector
Table top experiment: less than 2 m long.
Combines magnetic, TOF and calorimetric measurements
Secondary fragmentation on detector as low as possible
Beam monitor
Drift chamber
Start
counter
Permanent
Magnet (0.8 T)
Drift Chamber
BGO calorimeter
Plastic Scint.
DE/DX & TOF
Silicon trackers
Target

## Slide 16: The FOOT Detector
Table top experiment: less than 2 m long.
Combines magnetic, TOF and calorimetric measurements
Secondary fragmentation on detector as low as possible
Beam monitor
Drift chamber
Start
counter
Permanent
Magnet (0.8 T)
Drift Chamber
BGO calorimeter
Plastic Scint.
DE/DX & TOF
Silicon trackers
Target

## Slide 17: The FOOT Detector
Table top experiment: less than 2 m long.
Combines magnetic, TOF and calorimetric measurements
Secondary fragmentation on detector as low as possible
Beam monitor
Drift chamber
Start
counter
Permanent
Magnet (0.8 T)
Drift Chamber
BGO calorimeter
Plastic Scint.
DE/DX & TOF
Silicon trackers
Target

## Slide 18: FOOT : momentum measurement
Target
Silicon Pixel
Detector
Drift
chamber
Permanent
Magnet (0.8 T)
Drift
chamber
1 vertex + 1 tracking silicon pixel detector: MAPS MIMOSA 28 silicon pixel (20x20 mm)
2 drift chambers : UV 6+6 and 8+8 planes Ar/CO2
2 dipole permanent magnets Halbach geometry 0.8 T
Accuracy goal:
Δp/p ~3%

## Slide 19: ΔE/TOF detector and Calorimeter
360 BGO crystals 2 x 2 x 7 cm3
22 Y bars + 22 X bars
2 cm x 42 cm x 3 mm
TOF measurement below 100ps with heavy fragments: MEG-like digitizers
Charge mis-ID below the 2% level for Z=8 fragment at β~0.6
Scintillator type:
EJ-232

## Slide 20: Resolution goals
σTOF ~ 100 ps
σp/p ~ 4 % for Ekin ~ 200 MeV/u
σE/E ~ 2- 3% for Ekin ~ 200 MeV/u
σΔE/ΔE ~ 3%

## Slide 21: Evaluation of Energy Resolution in Inverse Kinematics (MC)
16O beam 200 MeV/u on C target assuming Δp/p ~ 4%
Preliminary!

## Slide 22: Evaluation of Xsec Resolution in Inverse Kinematics (MC)
16O beam 200 MeV/u on C target
Preliminary!

## Slide 23: light fragments (p, He): FOOT with emulsions
Tracking procedure at large angle, up to 750 with respect to the beam direction, has been developed at Napoli (OPERA)
The emulsion chamber must be exposed with a remotely controlled movement to avoid local pile-up
Must be run inside FOOT with Start counter and Beam monitor for absolute flux normalization
Particularly suited for radioprotection in space related measurement
G. De Lellis et al. JINST 2, 2007, P06004
Emulsion run could be the first data taking of FOOT in 2018

## Slide 24: Emulsions and light fragments
Tracking procedure at large angle, up to 750 with respect to the beam direction, has been developed at Napoli (OPERA)
The emulsion chamber must be exposed with a remotely controlled movement to avoid local pile-up
Must be run inside FOOT with Start counter and Beam monitor for absolute flux normalization
Particularly suited for radioprotection in space related measurement
G. De Lellis et al. JINST 2, 2007, P06004
Emulsion run could be the first data taking of FOOT in 2018

## Slide 25: Where can we lay down FOOT?
C,O (N) beams in the 100-350 MeV/u energy range availability
Possibility to mount and calibrate the experimental setup before data taking for “long” time (1-2 week)
Beam time availability in the week time range -> dedicated experimental hall
Several data taking period possible, with safe time schedule to be known in advance
CNAO Experimental room is our choice. Explicit interest and participation in the FOOT project. Exp. Hall ready by 2019
HIT: possible B plan, experimental room a bit small
GSI ?
Trento proton beam and LNS ion beams are fundamental for calibration purpose
Wish-list for an experimental facility:

## Slide 26: Projectile Fragmentation. Existing thin target, Double Diff Cross Section C-C measurements
LNS 62AMeV C beam
(2009)
GANIL 95AMeV C beam - E600 exp. (2011)
GSI 400MeV C beam
(2011): to be repeated
The community is interested for the 12C beam therapy, to explore the region 150-350 AMeV ( i.e. 5-17 cm of range in tissue…)
GANIL 50AMeV C beam

## Slide 27: Timeline & measurements program
Experimental program of FOOT:
Target fragmentation of p on O,C @100-200 MeV/u
Projectile fragmentation of O on C @200-400 MeV/u
Projectile fragmentation of C on C @200-350 MeV/u
Evaluation of production of some β+ emitters production (for example 8B) from C,O on C @200-400 MeV/u: useful for range monitoring of Particle Therapy
Fragmentation measurement of several beam on (C2H4)n of interest for radioprotection in space
In a realistic (moderately optimistic) schedule at least the a),b) measurements should start by 2019-2020

## Slide 28: FOOT collaboration in pills
Starting collaboration, funded by INFN for 2017, with contribution of Centro Fermi Institute
INFN Sections/Labs: Bologna, Frascati, Milano, Napoli, Perugia, Pisa, Roma1, Roma2, Torino, Trento
CNAO Collaboration
People: ~50 researcher
DATA taking foreseen @ CNAO/Heidelberg/GSI in 2020
International collaborations: Nagoya Univ.; GSI under discussion; open to other groups and institutions
Parallel NCTP modeling radiobiology activity within INFN: MoVE-IT (Modeling and Verification for Ion beam Treatment planning)

## Slide 29: Conclusions
The issue of the proton RBE (and of the target fragmentation) is under the spot in the Particle Therapy community
The FOOT collaboration is designing a detector to measure both target fragmentation in proton therapy and projectile fragmentation in carbon therapy
The R&D for experiment during 2017 has been approved and funded by INFN, with contribution by Centro Fermi Institute. Final approval for the 2018-2021 period expected in june 2017
Initiative in the starting phase and open to collaborations
Datat taking foreseen in late 2019 - 2020

## Slide 30: Thanks for your attention
M. Franchini, M. Negrini, G. Sartorelli M. Selvi, R. Spighi, M. Villa (INFN & Univ. Bologna); A. Sarti, E. Spiriti, M. Toppi (INFN-LNF); G. Battistoni, I. Mattei, S. Muraro, S. Valle (INFN Milano); G. De Lellis, A. Lauria, A. Di Crescenzo, M.C. Montesi,
V. Tioukov, G. Galai, A. Buonaura (INFN & Univ. Napoli Federico II); L. Servoli,
M. Salvatore (INFN & Univ. Perugia); D. Barbosa, N. Belcari, G. Bisogni,
N. Camarlinghi, M. Morrocchi, A. Retico, V. Rosso, G. Sportelli (INFN & Univ. Pisa); R. Faccini, F. Ferroni, V. Patera, R. Paramatti, A. Schiavi, A. Sciubba, G. Traini (INFN & Univ. Roma La Sapienza); M.C. Morone, G. De Vitis (INFN & Univ. Roma Tor Vergata); M.Durante, F. Tommasino, S. Hild, M. Rovituso, P. Spinnato, E. Scifoni,
C. Latessa (INFN & Univ. Trento); S. Argiro, P. Cerello, V. Ferrero, G. Giraudo,
N. Pastrone, C. Peroni, L. Ramello, M. Sitta (INFN & Univ. Torino); O. Sato (Nagpya Univ.); M. Pullia (CNAO, Pavia)
http://web.infn.it/f00t/index.php

## Slide 31: TOF & dE/dx measurement
A grid of 400x20x2.5 mm3 scintillator plastic slabs (XY) can give a very good ΔE ( -> Z ID) and TOF measurement.
TOF measurement below 100ps with heavy fragments: MEG-like digitizers
Charge mis-ID below the 2% level for Z=8 fragment at β~0.6
Marrocchesi et al,
NIM A 659 (2011) 477–483
Modest scintillation light saturation at low Z
Si detector signal
Plastic scint signal
Tested with similar fragment energies and experimental setup
ADC counts

## Slide 32: FOOT Calorimeter
TOF asks for 1.2 m lever arm -> R = 20 cm with 100 angular aperture of the fragments
A 2x2 cm2 granularity is due to the minimum track separation (1deg)
Thickness must contain the heavier fragment @ 200 MeV/u -> 7-10 cm
2x2x7 cm3 BGO units -> 300 channels
Read-out: not critical due to the high light yield (PMT, APD, SiPM)
4He
16O
12C
11B
9Be
7Li
Frag. range in BGO @200 MeV/u
The calorimeter shape and material choice is dictated by the heavy fragment range and the needed 2-3% energy resolution -> BGO.
Main challenge: neutrons leak out
FOOT Calorimeter length

## Slide 33: Halbach geometry for permanent magnet
Halback geometry provides uniform transverse magnetic field in a cylindrical geometry: B field proportional to ln(Rout/Rin)
B=0.8T
Thick=8cm
Rin=3.5 cm