## Slide 1: The muon g-2/EDM experiment at J-PARC
June 26, 2017
Tsutomu Mibe (IPNS/KEK)
for the J-PARC g-2/EDM collaboration
Photo of “muon cooling” experiment at TRIUMF M15
June 23-July 11, 2017

## Slide 2: Experimental determination of aμ = (g-2)/2
aμ = (g-2)/2
ωa : anomalous spin precession frequency
ωp : proton’s Lamor precession frequency
Present uncertainty ~ 120ppb (direct) (LANL)
~ 30ppb (indirect from HFS, assuming SM)
 60ppb (direct, J-PARC MuSEUM goal)
Present : 0.54ppm (BNL)
 140ppb
(FNAL/J-PARC goal)
(400ppb
(J-PARC phase-I))

## Slide 3: muon g-2 and EDM measurements
In uniform magnetic field, muon spin rotates ahead of momentum due to g-2 = 0
BNL E821 approach
γ=30 (P=3 GeV/c)
J-PARC approach
E = 0 at any γ
J-PARC E34
general form of spin precession vector:
FNAL E989

## Slide 4: Muon beam
Conventional muon beam
proton
π+
μ+
pion
production
decay
emittance
~1000π mm・mrad
Strong focusing
Muon loss
BG π contamination

## Slide 5: Muon beam
Ultra-cold
muon beam
Conventional muon beam
proton
π+
μ+
pion
production
decay
cooling
μ+
emittance
~1000π mm・mrad
emittance
1π mm・mrad
Strong focusing
Muon loss
BG π contamination
Free from any of these

## Slide 6: Ultra-cold Muon
Requirement for zero E-field:
Muons should be kept stored without E-focusing
 Beam with ultra-small transverse dispersion,
i.e. ΔpT/p ~0
28MeV/c
3 keV/c
re-acceleration
300 MeV/c
p =
ΔpT/p ~3 keV / 300 MeV =1E-5
Laser resonant ionization of Mu (μ+e-)

## Slide 7: Ultra-cold Muon
Requirement for zero E-field:
Muons should be kept stored without E-focusing
 Beam with ultra-small transverse dispersion,
i.e. ΔpT/p ~0
28MeV/c
3 keV/c
re-acceleration
300 MeV/c
p =
ΔpT/p ~3 keV / 300 MeV =1E-5
Laser resonant ionization of Mu (μ+e-)
G. Marshall

## Slide 8
surface muon beam
Muonium
production
target
(Silica aerogel)
Muonium
at thermal energy

## Slide 9: Optimization of muonium production target at TRIUMF (June 23 – July 11, 2017)
See also previous publications
Prog. Theor. Exp. Phys. 091C01 (2014)
Prog. Theor. Exp. Phys. 103C01 (2013)

## Slide 10: The J-PARC g-2/EDM collaboration
Collaborators
  Proposal (2009） ７２
  Conceptual Design Report (2011） ９２
  Technical Design Report (2015) １３７
  Technical Design Report (rev.) (2016) １４４
９ countries, 49 institutions
  Canda, Japan, Korea, UK, USA, France, Russia, Czech, China

## Slide 11
Resonant Laser Ionization of Muonium
Production target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage
Silicon
Tracker
66 cm
Super Precision Storage Magnet
(3T, ~1ppm local precision)

## Slide 12
Bird’s eye photo in Feb. 2008
J-PARC Facility
(KEK/JAEA)
Material and Life Science
Facility
Neutrino Beam
To Kamioka
Main Ring
(30 GeV)
Hadron Hall
LINAC
3 GeV
Synchrotron

## Slide 13: Proposed experimental site
Parking lot
muon
production
target
sparation neutron
source
g-2/EDM
storage magnet
muon linac
H-Line
MuSEUM
DeeMe
Material and Life science Facility in J-PARC

## Slide 15
2016.8.17

## Slide 16: Completion of H-line shielding (fall, 2016) by MLF muon facility group
branch
surface muon
mu LINAC
MuSEUM (Mu-HFS, μμ/μp)
DeeMe (mu-e conv.)

## Slide 17: Beamline and muon accelerator at H-line
Q-magnets
RFQ
IH
Mu
production
Beam
diagnostics
detectors
J-PARC MLF
Experimental Hall
Solenoid
Beam
Blocker
H1 area
(MuSEUM/DeeMe)
Bend
magnet
Q-magnets
blocker
surface muon (4 MeV)
accelerated muon (25meV4.5 MeV)
Initial
Accel.

## Slide 18: Beamline and muon accelerator at H-line
Q-magnets
RFQ
IH
Mu
production
Beam
diagnostics
detectors
J-PARC MLF
Experimental Hall
Solenoid
Beam
Blocker
H1 area
(MuSEUM/DeeMe)
Bend
magnet
Q-magnets
blocker
surface muon (4 MeV)
accelerated muon (25meV4.5 MeV)
Initial
Accel.
Data taken in 2016
Data taken in 2016
Data taken in 2016
Prototype
Reserved

## Slide 19: Muon acceleration test at D-line
Scheduled at D2 area in this November.
Simulated beam profile
after acceleration
Tested in 2015B/2016AB
Tested in 2015B/2016AB
Prototype of J-PARC RFQ
(to be tested in 2017)

## Slide 20: Muon storage magnet and detector
Cryogenics
e+ tracking
detector
2900 mm
Muon storage orbit
Iron yoke
Super conducting coils
666 mm
20
20
20

## Slide 21: Demonstration of spiral injection with low-E electron beam in Tsukuba
Mini-solenoid
(102 G)
Electron gun
(112 keV/c)
Iinuma, Nakayama, Osawa, Rehman
400mm

## Slide 22: First observation of spiral track (nominal B-field)
Beam
entrance
Slide by H. Iinuma

## Slide 23: B-field shimming test with the MuSEUM magnet (1.7 T) at J-PARC

## Slide 24: Field shimming by iron arrays
After shimming
Before shimming
Plots by K. Sasaki
B(μT)
azimuthal angle (rad)
axial position (mm)
r = 140 mm
B(μT)
azimuthal angle (rad)
axial position (mm)
400 ppm
0.4 ppm
-600 ppm
-0.5 ppm

## Slide 25: Positron tracking detector
Funded to build
~1/3 of detector vanes
silicon
strip
sensors

## Slide 26: Experimental sequence
40ms (25 Hz)
~1μs
40 μs
Surface
muon beam
(28 MeV/c)
Thermal
muonium
(3keV/c)
Ultra-slow muon
(3keV/c)
Acceleration + injection
(300 MeV/c)
Storage and detection
(300 MeV/c)
~1ns
~3ns
laser ionization
μ+e+
μ+
μ+
Mu
μ+

## Slide 27: Expected time spectrum of e+ in me+nn decay
w
e+ decay time (sec)
p>200 MeV/c
dm=2E-20 e・cm
e+ decay time (sec)
Up-down asymmetry
number of e+
∝EDM
ω

## Slide 28: TDR
TDR describes a technical design to achieve measurement of muon g-2 and EDM beyond BNL E821 precision.
  BNL E821 J-PARC E34
  g-2: 0.46 ppm  0.37 ppm (0.1ppm)
  EDM: 0.9 x 10-19 ecm  1.3 x 10-21 ecm
prepared by 144 authors

## Slide 29: TDR focused review (Nov 15-16,2016)
Gerry Bunce # (program manager)
# BNL-E821
* FNAL-E989
#*
#* (co-spokesperson)
#
#*
#

## Slide 30: Recommendations
Develop a “fast track” plan to achieve the Phase-1 result in a timely and cost-effective manner to capitalize on possible windows of opportunity, while keeping open an upgrade plan to realize the Phase-2 experiment. This includes value engineering of all systems.
This committee finds that Phase-1 of the E34 experiment is technically ready for Stage-2 approval. This is subject to resolution of the remaining technical issues identified herein and optimization of cost and schedule in order to realize a timely result.

## Slide 31: Summary
New g-2/EDM experiment at J-PARC
  Ultra-cold muon beam
  Compact storage ring
R&D phase is ending.
  The TDR was reviewed by the focused review committee in Nov, 2016.
Construction phase is starting.
  Surface muon beamline under construction.
  ~3-3.5 years to start data taking when full funding is provided.

## Slide 32: Comparison of experiments
 | BNL E821 | J-PARC E34
muon momentum | 3.09 GeV/c | 0.3 GeV/c
storage ring radius | 7 m | 0.33 m
storage field | 1.5 T | 3.0 T
focusing field (n-index) | 0.14 (electric) | 1.5 E-4 (magnetic)
average field uniformity | ≈1 ppm | << 1ppm
(local uniformity) | ≈50 ppm | ≈1ppm
Injection | inflector + kick | spiral + kick
Injection efficiency | 3-5% | 80%
muon spin reversal | -- | pulse-to-pulse
positron measurement | calorimeters | tracking
positron acceptance* | 65% | ≈100%
muon polarization | ≈100% | ≈50%
events to 0.46 ppm | 9 x 109 | 5 x 1011
* in the energy region of interest

## Slide 33: Brief history
Date | Events
July, 2009 | LOI submitted to PAC8
January, 2010 | Proposal submitted to PAC9
January, 2012 | CDR submitted to PAC13, Milestones defined.
July, 2012 | Stage-1 status recommended by PAC15 Stage-1 status granted by the IPNS director
May, 2015 | TDR submitted to PAC
Oct, 2016 | Revised TDR submitted to PAC and FRC
Nov, 2016 | Focused review on technical design

## Slide 34: muon g-2/EDM theory workshop at J-PARC
54 participants from 12 countries
http://g-2.kek.jp/meetings/g-2ws_2016/

## Slide 35: Cross calibration of NMR probes at ANL
The magnet is up and running at 1.45T.
Absolute calibration probes was tested with the same B-field.
Supported by the US-Japan corporative research program.
Ken’ich Sasaki
(KEK)
Peter Winter
(ANL)
Koichiro Shimomura
(KEK)
Photo by T. Mibe

## Slide 36: ½ mechanical mockup of the muon storage vacuum chamber

## Slide 37: Mu Hyperfine Structure
Zeeman Splitting
n12+n34=DnHFS
n12-n34 ∝ mm/mp
m+
e-
m+
e-
4463 MHz
DnHFS: Mu Hyperfine Structure
Pure leptonic system
(No composite particle)
ZF
HF
Slide by K. Shimomura

## Slide 38: MuSEUM Collaboration
Y. Fukao, H. Iinuma, Y. Ikedo, R. Kadono , N. Kawamura, A. Koda,
K. M. Kojima, T. Mibe, Y. Miyake, K. Nagamine, S. Nishimura,
K. Nishiyama, T. Ogitsu, R. Okubo, N. Saito, K. Sasaki,
K. Shimomura, P. Strasser, M. Sugano, A. Toyoda, K. Ueno,
A. Yamamoto, M. Yoshida
Y. Higashi, T. Higuchi, S. Kanda, Y. Matsuda, Y. Matsudate,
T. Mizutani, S. Seo, M. Tajima, K. S. Tanaka (currently @ Tohoku Univ.),
T. Tanaka, H. A. Torii, Y. Ueno, D. Yagi
K. Ishida, M. Iwasaki, O. Kamigaito
K. Kubo D. Kawall
M. Aoki, D. Tomono
E. Torikai
JAEA
T. U. Ito
Slide by K. Shimomura

## Slide 39: Resonance Measurement at B=0
Kr Gas Chamber
(RF Cavity inside)
Three layers of magnetic shield
Positron Counter
w/Al Absorber
Fiber Beam Profile Monitor
Muon Beam
200 mm
Slide by K. Shimomura

## Slide 40: First data at B=0 (2016A)
Muonium HFS resonance was observed
Fitted by Lorenzian and freq. center was 4463.1+-0.02 MHz
Expectation from precursor experiments is 4463.1 MHz
Frequency detuning (kHz)
Spin flip signal (%)
Slide by K. Shimomura
Ph.D thesis
S. Kanda
(2016)

## Slide 41: Resonance Lineshape at B=0 (2016B)
Frequency detuning (kHz)
Spin flip signal (%)
Statistical uncertainty ~ 4 kHz (x5 improvement)
More data to be collected in 2017
High-field data taking in preparation
Preliminary
Slide by K. Shimomura