## Slide 1
CMOS Active Pixel Sensors
A Novel Detection Technology for Particle Physics
Luciano Musa
57th International Winter Meeting on Nuclear Physics
Bormio (Italy), January 21-25, 2018
CERN – EP Department

## Slide 2
  Prelude
    Silicon detectors in HEP – a very brief historical excursus
  First Applications of CMOS pixel sensors to HEP experiments
    STAR Heavy Flavor Tracker
    ALICE Inner Tracking System
  Concepts for a future fast and lightweight heavy-ion detector
    Nearly 0-mass vertex detector
Outline
CERN – EP Department
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019

## Slide 3
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Towards end of 1970’s: intensive R&D on devices which could measure short-lived particles (10-12 - 10-13 s)
R&D at CERN(A) and Pisa(B) demonstrated that strip detectors (100-200mm pitch):
  high detection efficiency (>99%), good spatial resolution (~20mm) and good stability
  precise vertex reconstruction
However: fabrication of these devises was very tricky, thus limiting their availability
1980 – fabrication of silicon detectors using standard IC planar process (PIN diode  mstrip detector)
First use of silicon strips detectors by NA11(CERN SPS) and E706 (FNAL)
NA11 (1981): 6 planes (24 x 36mm2): resistivity 2-3 kWcm, thickness 280mm, pitch 20mm
(B) E706 (1982): 4 planes (3x3 cm2) + 2 planes (5x5cm2)
J. Kemmer, et al., “Development of 10-micrometer resolution silicon counters for charm signature observation with the ACCMOR spectrometer”, Proceedings of Silicon Detectors for High Energy Physics, Nucl. Instr. and Meth. 169 (1980) 499.
(A)
(B)
The rise of silicon detectors in HEP
Erik Heine, Joseph Kemmer and Gherard Lutz: 2017 EPS prize for “Outstanding Contributions to HEP” (pioneering the development of silicon mstrip)

## Slide 4
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
The rise of silicon detectors in HEP
The next step forward came with the advent of the VLSI technology that allowed coupling ASIC amplifier chips directly to the detectors
1990s - LEP, first silicon vertex detectors were installed in DELPHI and ALEPH experiments, then OPAL and L3
1989 - first DELPHI vertex detector, consisting of two layers of single-sided strip detectors
Projective geometry  ambiguity at high multiplicities (high occupancy)
This started to become apparent already at DELPHI:
High number of ambiguities  reconstruction efficiency suffered a lot, especially in the forward direction
Not usable close to IP in hadron colliders (LHC) or HI experiments at SPS
Another problem at (very) high particle load  degradation of the sensor by the high radiation dose
This implies starting with a very large signal-to-noise ratio, which can only be obtained with detector with small capacitance

## Slide 5
The Inception of Silicon Pixel Detectors
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
“The silicon micropattern detector: a dream?”
E.H.M Heijine, P. Jarron, A. Olsen and N. Redaelli , Nucl. Instrum. Meth. A 273 (1988) 615
“Development of silicon micropattern detectors”
CERN RD19 collaboration, Nucl. Instrum. Meth. A 348 (1994) 399
1995 – First Hybrid Pixel detector installed in WA97 (CERN, Omega facility)
1996/97 – First Collider Hybrid Pixel Detector installed in DELPHI (CERN, LEP)
Work carried out by RD19 for WA97 and NA57/CERN
CERN – WA97 Experiment (1995)
5 x 5 cm2 area
7 detector planes
~0.5 M pixels
Pixel size 75 x 500 mm2
1 kHz trigger rate
Omega2 chip
E. Heijne, E. Chesi
No-field, Pb-Pb, 153 reconstructed tracks
Hybrid pixel detector

## Slide 6
Pixel Detectors at the LHC
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Parameters | ALICE | ATLAS | CMS
Nr. layers | 2 | 3 | 3
Radial coverage [mm] | 39 - 76 | 50 - 120 | 44 – 102
Nr of pixels | 9.8 M | 80 M | 66 M
Surface [m2] | 0.21 | 1.7 | 1
Cell size (rf x z) [mm2] | 50 x 425 | 50 x 400 | 100 x 150
Silicon thickness (sens. + ASIC) - x/X0 [%] | 0.21 + 0.16 | 0.27 + 0.19 | 0.30 + 0.19
ATLAS Pixels
CMS Pixels
ALICE Pixels
10 years after the first use in WA97… hybrid pixel detectors at the heart of the LHC experiments

## Slide 7
Beyond Hybrid Pixel Detectors …
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Hybrid Pixel Detector
Monolithic Pixel Detector
N. Wermes (Univ. of Bonn)
N. Wermes (Univ. of Bonn)
Since the very beginning of pixel development (CERN RD 19):
Motivation to reduce: cost, power, material budget, assembly and integration complexity
Several major obstacles to overcome:
CMOS generally not available on high resistivity silicon (needed as bulk material for the sensor)
Full CMOS circuitry not possible within the pixel area (only one type of transistor  slow readout)
dream to integrate sensor and readout electronics in one chip
✔
✔
MAPS exist in many different flavors: CMOS, HV CMOS, DEPFET, SOI
The following will cover only CMOS Active Pixel Sensors (CMOS MAPS) = CMOS Active Pixel Sensors (CMOS APS)

## Slide 8
ALICE LS2 Upgrade
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Owing to the industrial development of CMOS imaging sensors and the intensive R&D by HEP community
STAR HFT
0.16 m2 – 356 M pixels
CBM MVD
0.08 m2 – 146 M pixel
ALICE ITS Upgrade (and MFT)
10 m2 – 12 G pixel
Mimosa-1
Mimosa-2
Mimosa-3
Mimosa-26
2.7 cm2
(EUDET Telescope)
. . .
… several HI experiments have selected CMOS pixel sensors for their inner trackers and intensive R&D for ATLAS
2014 - First CPS Detector
Cherwell
ALPIDE
sPHENIX
0.2 m2 – 251 M pixel
…

## Slide 9
p-type crystalline epitaxial layer hosts n-well charge collector
Signal is generated in a high-resistivity (> 1 kWcm) epi-layer ~20mm thick (larger values possible)
~80 e-h pairs per micron
Only one transistor type in the active area (NMOS)
Use rolling shutter architecture for matrix analogue readout
Early versions with thin and low resistivity epi-layer
epi-layer not fully depleted
Charge collected (mostly) by diffusion and drift
Long charge collection time
Sensitive to radiation induced displacement damage in the epi layer (ok for applications with up to ~ 1012 1MeV Neq/cm2)
Rolling Shutter Architecture
TH
TH
TH
TH
TH
TH
TH
TH
SEL = 1
2
2x
SUZE (Zero Suppression and Encoding)
AMP
rolling
shutter
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
CMOS MAPS – state-of-the-art in 2010

## Slide 10
First application to Vertex Detectors
Measurement of short-lived particles in nuclear-nuclear collisions
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019

## Slide 11
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Example: D0 meson
Analysis based on invariant mass, PID and decay topology
Particle | Decay Channel | c (m)
D0 | K + (3.8%) | 123
D+ | K + + (9.5%) | 312
 | K+ K + (5.2%) | 150
 | p K + (5.0%) | 60
Open charm
K-
π+
D0 flight line
D0 reconstructed
momentum
Primary vertex
A
A
d0k
d0π
secondary
vertex
Pointing
Angle θ
~ 100 μm
Secondary Vertex Determination

## Slide 12
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Invariant mass distribution of K-p+ pairs before and after applying selection criteria on the relation between the secondary (D0 decay) and primary vertices
ALICE, Int. J. Mod. Phys. A 29 (2014) 1430044
Analysis based on invariant mass, PID and decay topology
K-
π+
D0 flight line
D0 reconstructed
momentum
Primary vertex
Pb
Pb
d0k
d0π
secondary
vertex
Pointing
Angle θ
~ 100 μm
Example: D0 meson
Secondary Vertex Determination

## Slide 13
detector layer 1
detector layer 2
pointing resolution = (5  22GeV/pc) m
From detector position error
From Coulomb scattering
r2
r1
true vertex
perceived
vertex
x
x
v
r2
r1
true vertex
perceived
vertex
v
m
expectations for the ITS upgraded 
first pixel layer
Vertex projection from two points: a simplified approach (telescope equation)
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
What determines the Impact parameter Resolution?

## Slide 14
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Mechanical support with kinematic mounts (insertion side)
Physics Runs in 2015-2016
Aluminum conductor Ladder Flex Cable
Ladder with 10 MAPS sensors (~ 2×2 cm2 each)
2 layers
10 sectors total (in 2 halves)
4 ladders/sector
RDO Buffers / Drivers
MAPS
2-layer kapton flex cable with Al traces
Key dates
3-sector prototype May 2013
Full detector Jan 2014
MAPS
power ~ 160mW/cm2
Rolling Shutter
~180ms integr. time
STAR Pixel Detector – First application of CMOS APS to HEP

## Slide 15
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
DCA pointing resolution
  46 µm for 750 MeV/c Kaons
  ~ 30 µm for p > 1 GeV/c
D0  K  production in √sNN = 200GeV Au+Au collisions
46 µm
STAR Pixel Detector – Performance

## Slide 16
|B| = 0.5 T
New Inner Tracking System (ITS)
CMOS Pixels
g improved resolution, less material, faster readout
Novel MAPS technology
New Inner Tracking System based on CMOS sensors for ALICE
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019

## Slide 17
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
147 cm
40cm
Closer to IP: 39mm  22mm
Thinner: ~1.14%  ~ 0.3% (for inner layers)
Smaller pixels: 50mm x 425mm  27mm x 29mm
Increase granularity: 20 chan/cm3  2k pixel/cm3
Faster readout: x 102 Pb-Pb, x 103 pp
10 m2 active silicon area: 12.5 G-pixels, s ≈ 5mm
will be used (or it is proposed) for several other HEP detectors and non HEP applications
NICA MPD (@JINR)
sPHENIX (BNL)
proton CT (tracking)
CSES – HEPD2
New ITS
ALPIDE (ALICE Pixel Detector) - Developed for the ALICE upgrade (ITS and MFT)
…
1.5 ≤ h ≤ 1.5
A new ITS: closer to IP, thinner, higher position resolution

## Slide 18
Pointing Resolution
x 3
X 6
~40 μm at pT = 500 MeV/c
Impact parameter resolution
Total weight
1.4 grams
Tracking efficiency
Tracking efficiency (ITS standalone)
pions
A new ITS: closer to IP, thinner, higher position resolution
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019

## Slide 19
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
CMOS Pixel Sensor using 0.18mm CMOS Imaging Process
NA ~ 1018
NA ~ 1016
NA ~ 1013
High-resistivity (> 1kW cm) p-type epitaxial layer (25mm) on p-type substrate
Small n-well diode (2 mm diameter), ~100 times smaller than pixel => low capacitance (~fF)
Reverse bias voltage (-6V < VBB < 0V) to substrate (contact from the top) to increase depletion zone around NWELL collection diode
Deep PWELL shields NWELL of PMOS transistors
NA ~ 1018
NA ~ 1013
Artistic view of a SEM picture of ALPIDE cross section
 full CMOS circuitry within active area
pixel capacitance ≈5 fF (@ Vbb = -3 V)
Cin ≈ 5 fF
2 x 2 pixel
volume
Qin (MIP) ≈ 1300 e a V ≈ 40mV
collection electrode
28 mm
ALICE CMOS Pixel Sensor

## Slide 20
20
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Blank Wafers QA at TMEC (SRP and XSEM measurements)
1 kWcm
Wafer thickness 97.22mm
High-res epi: 25.28mm
ALICE CMOS Pixel Sensor

## Slide 21
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Low capacitance  large S/N at low power
NWELL DIODE output signal = Q /C
Minimize spread of charge over many pixels
minimize capacitance:
 small diode surface
 large depletion volume
Explorer chip (ALICE R&D)
Silicon strip capacitance: > 10 pF (~1.5 pF / cm)
Hybrid pixel capacitance: ~300 fF
MAPS “small electrode” pixel capacitance: < 5 fF
Cd = 1fF: 1300 e-  200mV (almost a digital signal)
ALICE CMOS Pixel Sensor

## Slide 22
pads over matrix
zero suppression
zero suppression
zero suppression
zero suppression
Bias, Data Buffering, Interface
THR
COMP
AMP
1024 pixel columns
signal processing circuitry integrated in pixel matrix
512 rows
50mm thick
130,000 pixels / cm2 27x29x25 mm3
charge collection time <30ns (Vbb = -3V)
Max particle rate: 100 MHz/cm2
fake-hit rate: < 1 Hz/ cm2
power : ≈300 nW /pixel (<40mW/cm2)
Matrix Layout
Pixel Layout
pixel matrix
periphery
4 pixels
4 pixels
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)

## Slide 23
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)
Nucl. Phys. A 967 (2017) 900-903
10x lifetime NIEL
Non irradiated
Large operational margin with only 10 masked pixels (0.002%), fake-hit rate < 2 x 10-11 pixel/event
Non irradiated and TID/NIEL chips similar performance
5 mm resolution @ 200 e- threshold
Chip-to-chip negligible fluctuations
6 GeV/c p
6 GeV/c p
99%
Nucl. Phys. A 967 (2017) 900-903

## Slide 24
ALICE PIxel DEtector (ALPIDE)
Sensors
Inner Barrel is built at CERN
ALICIA - High-precision automated machine
Sensor test and HIC assembly
using ALICIA machine
150 µm
pixel matrix
100 µm
pixel matrix
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019

## Slide 25
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)

## Slide 26
Inner Barrel Production completed and all layers assembled
Single stave, perpendicular tracks
Tilted staves with overlap, inclined tracks
Inner half-barrel
Material budget
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)

## Slide 27
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)
102 Million pixel, average noise uniform ~ 5e
Layer-6
Layer-4

## Slide 28
Ultra-lightweight Vertex Detector
Approaching 0-mass detector
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019

## Slide 29
Single stave, perpendicular tracks
Tilted staves with overlap, inclined tracks
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
147 cm
40 cm
ITS2
Space Frame
Cold Plate
Cooling Pipe
9 Pixel Sensors
Flex Printed Circuit
Inner half-barrel
ALICE ITS2 Material Budget
Silicon 14%

## Slide 30
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
How to further reduce material budget?
Eliminate active cooling …
… replace with low forced air flow (< 3 m/s)
viable for power densities below 20mW/cm2
Eliminate electrical substrate
Possible if sensor covers the full stave length
ALPIDE Chip: pixel matrix power 7mW/cm2 … … the rest (~33mW/cm2) is dissipated by the peripheral circuitry
a Can we put the circuit periphery at the periphery of the detector?
Space Frame
Cold Plate
Cooling Ducts
Flex Printed Circuit
9 Pixel Sensors
pixel matrix
periphery
Can we further reduce the material budget?

## Slide 31
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
CMOS photolithographic process
defines wafer reticles size
Typical field of view O(2 x 2 cm2)
Reticle is stepped across the wafers to create multiple identical images of the circuit(s)
Stitching allows fabrication of sensors larger than the reticle size
14cm
Courtesy: R. Turchetta, Rutherford Appleton Laboratory
staves built by tiling several sensors
27cm
Stitching allows the fabrication of wafer scale sensors

## Slide 32
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Silicon Genesis: 20 micron thick wafer
Can we exploit flexible nature of thin silicon ?
Chipworks: 30µm-thick RF-SOI CMOS
Ultra-thin chip (<50 um): flexible with good stability
van den Ende DA et al. Mechanical and electrical properties of ultra-thin chips and flexible electronics assemblies during bending.
Mircoelectron reliab (2014), http://dx.doi.org/10.1016/j.microrel.2014.07.125
Ultra-thin curved silicon chips

## Slide 33
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Vertex Detector (innermost 3 layers)
Beampipe
IR 16 mm
DR 0.5mm
Pipe: r ≈ 16mm , DR = 0.5mm
L0: r ≈ 18mm , L1: r ≈ 24mm. L2: r ≈ 30 mm
Truly cylindrical vertex detector
0.05% x/X0 per layer
Open cell carbon foam
Open cell carbon foam
Layers supported by high-thermal conductive carbon foam

## Slide 34
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ITS3 – System Integration
Detector and service integration similar to ITS2

## Slide 35
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Tracking Performance
Pointing resolution (pions): ≈ 10 mm @ 1 GeV/c, <50mm @ 200 MeV/c
B = 0.5 Tesla
IT (L0 , L1, L2)
beam pipe (BP)
IT inside BP
2.8cm
IT outside BP
1.6cm
IT inside BP
R. Shahoyan - 2018

## Slide 36
The use of CMOS imaging technologies opens new opportunities
Ultra-lightweight vertex detectors, large area tracking detectors and digital calorimeters
  a Drastic reduction of power consumption and material budget
  enhanced performance (spatial and time resolution)
  a reduction of power consumption and material budget
  large cost saving due to low production costs wrt to conventional silicon strip and hybrid pixel technologies
Based on this technology, a concept for a nearly massless vertex detector (x/X0 <0.05%) has been developed by ALICE experiment for the study of heavy-flavor and low-mass dileptons in nuclear-nuclear collisions at the LHC
36
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
Concluding Remarks

## Slide 37
Thank You
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019

## Slide 38
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)
Analog front-end continuously active, acts as an analogue delay line (~1 µs peaking time)
Global threshold for discrimination => binary pulse OUT_D
Digital in-pixel circuitry with three hit storage registers (multi event buffer)
Global shutter (STROBE) latches the discriminated hits in next available register
Cdet~2.5 fF @ -3 Vbb
Cin~1.6 fF
3 in pixel Multi Event Buffers
In-pixel Pulsing (Analog/Digital)
Pixel masking
max hit rate (limited by input node)
~ 100 MHz / cm2

## Slide 39
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)
Thresholds and Noise
Thresholds
Noise
Noise Map
Thresholds MAP
noise in electrons
thresholds in electrons
S-curve scan using internal charge injection circuit
keep comparator threshold fixed
inject varying charges
extract threshold and noise from error-function fit

## Slide 40
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)
Reception test at CERN
Comparison between full stave and stand-alone chip
100 million pixels

## Slide 41
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019
ALICE PIxel DEtector (ALPIDE)
Detector Construction and Assembly
Module: till March/April 19
Staves: till Jul/Aug 19
Commissioning on ground with final services full detector operation 24/7
Installation
6-month Global Commissioning
Apr ‘19
Aug ‘19
May ‘20
Feb ‘21

## Slide 42
What’s next? - Future R&D opportunities using CMOS technologies
Extremely compact design
Small Moliere radius (RM = 10.5 ± 0.5mm)
High-Granularity Digital Calorimeter Prototype
R&D in the context of FoCal in ALICE
4 x 4 x 10 cm3 prototype
Prototype based on MIMOSA pixel chip
24 layers (1 X0 W + MIMOSA23)
39M pixels, 30mm pitch
Beam tests from 2 to 250 GeV/c (DESY, CERN PS & SPS)
Cosmic muons
Preparing next generation prototype with ALPIDE
Very good energy linearity and resolution
Extremely good position resolution
L. Musa (CERN) – International Winter Meeting on Nuclear Physics, Bormio, 8-11 Jan 2019