## Slide 1: MUonE
U. Marconi
MUonE2022, 2022 November 14th

## Slide 2: Content
The MUonE project
Status of the detector, software and analysis tools
  2S modules
  Tracking system
  Data acquisition
  Electromagnetic calorimeter
  Software
  Analysis
Plans

## Slide 3: A novel method to measure Δαhad(t)
By 160 GeV muons hitting electrons at rest in a target of low Z material. A high intensity muon beam, the M2 muon beam, exists in CERN. Iμ ~ 2×108 muon/spill equivalent to ~40M muon/s
The collisions result in a boosted kinematics with scattering angles θμ < 5 mrad, θe < 30 mrad (Ee > 1 GeV) Angles have to be measured with respect to the incoming muon direction.
The shape of the differential cross section as a function of t = q2 ( q2 < 0 ) depends on the hadron running Δαhad(t)
θμ
θe
Target
incoming muon

## Slide 4: Correlation between the scattering angles
xpeak = 0.914
xmax = 0.932
At 150 GeV we could cover 87% of the integral for aμ

## Slide 5: The 2D angular distribution and the cross section
No effect here: the normalization region
f (θe,θμ) ⊗ Resolution
cross section

## Slide 6: Parameterization of the hadronic running

## Slide 7: Elastic events in the Test Beam of 2018

## Slide 8: The detector resolution

## Slide 9: The detector
muon spectrometer

## Slide 10: 2S modules
￼
Digital readout at 40 MHz
Expected resolution 22 μm
We use stubs i.e. trigger primitives for the CMS L1 trigger
x1
x1 + w
bottom sensor
top sensor

## Slide 11: The tracking station
Positions of the modules must be stable within 10 μm
Tilted X and Y modules to improve the resolution
UV modules to solve reconstruction ambiguities

## Slide 12: To improve the spatial resolution
By tilting the module we do expect to improve the resolution: 22 μm →10 μm The tilting angle is 14 degrees

## Slide 13: 2S module on its frame
The support structure in INVAR
Very expensive
Difficult to machine

## Slide 14: Status of the CMS 2S modules
Four 2S modules assembled in Perugia.
First 2 built in 2021 and successfully tested in the first MUonE-CMS combined test performed in November 2021
The second pair of modules built in 2022 show problems:
  Module-3: is presently unusable, because of electronics problems appeared after the assembling. It has to be returned to Perugia to try fixing the issue. The same problem has been observed in the Bruxelles laboratory.
  Modules-4: half the module is effectively working. It’s a well known problem due to a faulty CIC. A fix exists and it’s relatively easy to apply.
A fifth module could be built, but again there is an issue with the electronics.

## Slide 15: Tracker beam test setup
We managed to keep running for debugging the DAQ and testing the 2S modules available
The station placed on rails to allow easy movements in and out the M2 beam

## Slide 16: Tracker beam test setup in M2
4 of 6 2S modules installed into the station
X and Y modules at front and back mounted
U, V modules in centre are missing
40 MHz readout to Serenity DAQ card, then 10 Gbps Ethernet link to PC
Data saved locally and on EOS
Still possible to take data using the beam halo 1kHz vs 10 MHz counting rate

## Slide 17: Test with a full station and a calorimeter (October ‘22)
A fully equipped tracking station and the calorimeter
One week of test in M2 as main users performed the last October
High intensity muon beam, up to 2×108 muon/spill, for the first time

## Slide 23: Synchronization
Need to ensure the sampling point for each module is in sync for any given muon
Asynchronous beam: no absolute timing reference
Method: for a pair of modules take time difference in BX between captured stubs in each module: the first module is taken as reference, next modules checked in comparison. Check delta as function of DLL settings and plot the mean at each setting
The procedure can correct for offsets in the modules to maximise detetction efficiency to 0.5 ns

## Slide 25: Mechanical Survey
Fiducial markers ordered (2 spheres, 1/2 inch)
Design of the aluminum holders for spheres done
To set the alignment initial conditions

## Slide 26: The holographic system
Laser interferometry of rays going through different paths
It allows monitoring the position of two sensors with respect to a reference one with resolution of ~0.25 μm
To be used during alignment and data taking
The system is ready to monitor one station Extensible to a second station easily

## Slide 27: The holographic system (cont.)
Thermal load corresponding to a power of 2W applied to the mechanical structure of the Aluminium prototype. Module’s consumption ~5 W: cooling system foreseen.
Initial state
Steady power on
Power off
Estimated relative displacement between planes 1.5 μm

## Slide 28: ECAL

## Slide 29: ECAL tests in CERN’sT9
ECAL assembled and tested at the end of July in the CERN T9 electron beam line
Laser pulses

## Slide 30: ECAL test setup and DAQ
The FC7 FEBs are used to read out the digitizers and to transmit data to the PC through a 10 Gbps Ethernet link.
Self trigger modes, relying of the ECAL’s cells energy content and external trigger successfully exploited.
Counting rate capability ~1.5 kHz
The laser system confirmed to be crucial for settings and monitoring the stability of the channels
The readout
External trigger
Beam scintillators and Cherenkov counters

## Slide 32: ECAL test setup: main achievements
The light yields have to be improved: the APD-PbWO4 optical coupling has to match.
Electronic noise has to be reduced: the analysis of the main sources is ongoing.
Cooling of the ADPs was not entirely satisfactory
The monitoring system of the APD temperature has to be improved/replaced
Laser stability is monitored by a dedicated Photodiode, whose output signals has to be registered for reference checks
4 GeV electrons
Laser pulses

## Slide 33: Software
FairMUonE: FairRoot based software, for generation, simulation, digitization and reconstruction
Event generation: NLO Mesmer generator for μ - e scattering Accurate beam profile description
Simulation: Geant4 v10.7.1 implemented in FairRoot Detailed geometry description implemented, scalable to any number of stations Common geometry files (.yaml files) for simulation/digitization/reconstruction
Digitization: Digitization for tracking stations ready Realistic electronic noise and channel cross-talk added Calorimeter digitization is ongoing

## Slide 34: Software (cont.)
Track reconstruction: Kalman filter for tracking implemented Tracking efficiency studies ongoing: Allowing shared hits improves track reconstruction efficiency dramatically in the whole energy range
Vertex reconstruction: Kinematic fit constraining three tracks to meet in the middle of a given target Adaptive vertex fitter developed for the alignment

## Slide 35: Detector alignment
Initial conditions set by means of the mechanical survey: Δz ~ 50 - 100 μm
Software alignment shall reach the ultimate precision
Alignment parameters will be determined by minimizing the global χ2 MUonE is perfectly suited for the global χ2 approach because of the linearity.
Residuals ρ depend on the alignment parameters α as well as track parameters π
The required precision for the alignment is Δz ~ 10 μm
How to get the longitudinal scale to such a precision? Use thin targets located to a known distance and reconstruct vertices from these targets to gauge the scale

## Slide 36: Detector alignment (cont.)
Design and construction of the targets system by the CERN accelerator group
Use pion beams to enhance the multiplicity of tracks from the vertices in the thin targets
Use the adaptive vertex fitter to determine the vertices positions
Use the global alignment method to get the alignment parameters

## Slide 37: Analysis
For a detailed description of the analysis strategy see: G.Abbiendi, Phys. Scr. 97 (2022) 054007 [arXiv: 2201.13177]
Template fit of the 2D distribution using the CMS Combine tool: Fit with systematic effects included as nuisance parameters, and extracted along with the signal parameters.
Use normalization region to calibrate the larger systematic effects: beam energy, angular intrinsic resolution.
MESMER MC + fast detector simulation
to generate template distributions.
Combine analysis tool to perform the combined likelihood fit to the signal and systematics.

## Slide 38: Plans
Prove the feasibility of the proposed MUonE method in 2023
Detect elastic scattering at 40 MHz
  Reconstruction efficiency
  Background studies
Study the alignment in test beams to then measure the beam energy
Integrate ECAL and correlate its response to the tracker
Write the experimental proposal
Move to the experiment with 10 stations to get a first measurement before the LS3