## Slide 1
60th International Winter Meeting on Nuclear Physics Bormio, Italy, January 2024
Kaon-nucleon/nuclei strong interaction studies at the DAɸNE Collider: a strangeness journey
Mihail Antoniu Iliescu

## Slide 2
2
DANE collider
SIDDHARTA is set up here
Electron-positron collider, tuned at F resonance, which is produced nearly at rest (F Factory)
-boost: 55 mrad crossing angle → 28 MeV/c
-Φ production cross section ~ 3000 nb (loss-corrected)‏
-Integral luminosity ~ 7 pb-1 per day 1) (~ 107 K± )‏, crab waist optics
Peak luminosity ~ 4 × 1032 cm-2 s-1 = 550 Hz K±
Lifetime ~ 20 min, high background during injections.
F Decays in k+k− (48.9%±0.5%), k0Sk0L (34.2%±0.4%),
ρ + π / π+ + π⁰ + π⁻ (15%)
Studies completed or ongoing:
Neutral channel - CP Violation, rare decays (KLOE)
Charged -light kaonic atoms (DEAR, SIDDHARTA, SIDDHARTA-2)
-Hypernuclei (FINUDA)
-k (multi)nucleon absorption, L1405
nature (AMADEUS)
Proposed studies:
-extensive light kaonic atoms (EXCALIBUR)
-charged kaon mass measurement
-low energy k+ N scattering

## Slide 4
The strong interaction width >> E.M. radiative transition width
The level shift is of the same order of magnitude ->
direct information about the scattering amplitude at threshold
Kaonic atom processes
K-
e-
Auger Electron
2) Cascade
1) Capture
3) Strong interaction
5) Nuclear absorption
X-ray
e.g.
1s for K-p, K-d
2p for K-He
highly-excited state
Collision induced
de-excitation
n ~ sqrt(M*/me) n’ ~ 25 (for K-p)
(M* : K-p reduced mass)
0) Moderated, then stopped in a target medium
4) Radiative transition
If survives to Stark mixing effect 
On the lowest levels
Auger

## Slide 5
Kaonic Hydrogen – Deser formula
__
With a0, a1 standing for the I=0,1 S-wave KN complex scattering lengths in the isospin limit (md = mu),  being the reduced mass of the K-p system, and neglecting isospin-breaking corrections, the relation reads:
… a linear combination of the isospin
scattering lengths a0 and a1;
to disentangle them, the kaonic deuterium
scattering length is needed, as well
1Meißner,Raha,Rusetsky, 2004
‘‘By using the non-relativistic effective Lagrangian approach a complete
expression for the isospin-breaking corrections can be obtained;
in leading order parameter-free modified Deser-type relations exist and
can be used to extract scattering lenghts from kaonic atom data“1

## Slide 6
Kaonic Hydrogen X-ray measurements summary
Repulsive type
Attractive
DEAR
SIDDHARTA

## Slide 7
Improved constraints on chiral SU(3) dynamics from kaonic hydrogen
Y. Ikeda, T. Hyodo and W. Weise, PLB 706 (2011) 63

## Slide 8
Kaonic deuterium
For the determination of the isospin dependent scattering lengths a0 and a1 the hadronic shift and width of kaonic hydrogen and kaonic deuterium are necessary !
Elaborate procedures needed to connect the observables with the underlaying physics parameters.
larger
than
leading
term
SIDDHARTA-2
Achievable
precision
Kaonic deuterium predictions

## Slide 9
- Almost monochomatic Kaon beam from  decay => facilitates stopping the kaons in a small volume of gas at specific density => allows to produce the exotic atoms before kaon decay and enhace the detection efficiency for rare events. However, the boost induced by the beams crossing angle requires a compensating step degrader.
-Minimum beam-related hadronic background ( decays in 49% back-to-back charged and 31% neutral kaons)‏
-High luminosity (4 × 1032 cm-2 s-1 )
-is polarized, so the kaon flux emitted mostly on transverse plane to machine beam pipe (sin2 distribution)=> easier to capture a high fraction on a reduced solid angle
Why at DAΦNE?

## Slide 10
Experimental problems
-Asynchronous background: the transitions of interest are in the keV range; the final component of electromagnetic cascades produced in the accelerator pipe (and other setup materials) invested by e-/e+ lost from the beam overlaps the signal; each lost particle cascades down 5 orders of magnitude, while the loss rate in the interaction region reaches few MHz. This sums up to a total rate of ~1010 X-ray photons/s. The main contribution comes from Touschek effect.
-Synchronous background, associated to K absorption on materials nuclei, or to other decay channels. It can be considered a hadronic background.
-Spectra contamination by Xray fluorescence or by X-rays produced in higher transitions of other kaonic atoms, formed in the setup materials; this imposes a very restrictive choice of the materials to be used and high purities.
-Low energy kaons decay rate; the target geometry, related to the optimal gas density, shielding and trigger, results in a moderation kaon path of ~20-30 cm, through kapton and high density gas. Consequently, a fraction of kaons will decay before being captured.
-Survival of the exotic atom down to the last cascade step (to the 1s level): in the case of kaonic Hydrogen, only 1.2% of the atoms perform the 2p->1s transition, while for the kaonic Deuterium the theoretical estimates indicate only ~10-3 of them will reach the lowest state. The main reason is the Stark mixing effect.

## Slide 11
SIDDHARTA cryo target
The optimization of the target density took into account the balance between the Stark effect and kaon
stopping power. The chosen density was ~30x STP, which would require thick windows to stand
the high corresponding pressure. Since thick windows would not allow X-rays to reach the SDD
detectors, a cryogenic target was designed and build, operating near the H2 L.P. A 2-stage He expansion
cryostat grants the necessary cooling. In order to minimize the detector noise, the SDDs were also
operated under cryogenic conditions (~150K). The setup is under high vacuum insulation.
1 bar
SDD sockets
Yield estimates for kH and kD.Koike, Harada, and Akaishi, 1996

## Slide 12
The Semiconductor Drift Detector
Anode
The electrons are collected by the small anode,
characterized by a low output capacitance.
Advantages: very high energy resolution
at fast shaping times, due to the small anode
capacitance, independent of the active area of
the detector
Entrance window
ANODE
Fast X-ray detectors

## Slide 13
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
100
200
300
400
500
600
700
800
A (cm-2)
FWHM (eV)
SDD PIN Si(Li) 150 K 5.9 keV line
PIN Tsh=20us
Si(Li) Tsh=20us
SDD Tsh=1us
Spectroscopic resolution: detector comparison
Fast X-ray detectors

## Slide 14
144 SDD’s 1cm x 1cm

## Slide 15
SDD
front
end
Event timing
(R.T.)
SDD
front
end
SDD
front
end
Hit addr.&HT
Hit Edep.
Control signals &
threshold prog.
SDD
DAQ
SDD
array
2 x 3
K trigg.
electronics
Scintillator
arrays
Coincidence (R.T.)
Event Index (R.T.)
Edep.,Dt k-X, Addr., Index
T.O.F.,Edep., Addr., Index
K trigg.
DAQ
Full event info
“Clean” Kaonic X-ray event
Offline selection
(TOF1, TOF2,
Edep.K, H.T.,
topology, drift time)
DAFNE
injection
control
SIDDHARTA DAQ flow chart
Inhibit (R.T.)

## Slide 16
SIDDHARTA SETUP
(two scintillator arrays, timed by the DAFNE RF)‏
Dealing with the asynchronous (EM) background
Shielding and fast X-ray detectors, synchronized with the kaon trigger

## Slide 17
SIDDHARTA trigger
1 ns
2.8 ns
MIP’s
Kaons
Rejection factor >104
SDD Self trigger
MIP’s
Drift time
The trigger is generated by the coincidence of 2 back-to-back scintillators.
Further kaon ID is given by the specifc TOF, measured from the collision time, marked by RF.
SDD and kaon trigger

## Slide 18
Kaonic hydrogen
SIDDHARTA results

## Slide 19
Kaonic hydrogen and kaonic deuterium

## Slide 20
Kaonic hydrogen background subtracted spectrum
Energy (keV)‏
A simultaneous fit of KH and Kd spectrum was done, to get rid of the kaonic background lines (KO, KN). The overall integrated luminosity for the KH run was 290 pb-1.
For the signal component 8 voigtians with given gauss resolution
and free identical lorentz width were used for (2-1),.. (9-1)‏
transitions.
The relative positions follow a pattern fixed by the QED values.
The main intensities of (2-1),(3-1) and (4-1)‏ lines were left free,
while the higher transitions were coupled according to theoretical
expectations (cascade calculation, Koike‘s values)‏.
KH
(2-1)‏
KH
(3-1)‏
KH
(4-1),..
(9-1)‏
Note: Khigh
yield pattern
The backgound shape is determined by fitting the KD data and including the pattern function in the KH fit.
ε1s = -283 ± 36(stat) ± 6(syst) eV
Γ1s = 541 ± 89(stat) ± 22(syst) eV
Nuclear Physics A 881 (2012) 88–97

## Slide 21
SIDDHARTA-2 Monte Carlo
To compensate for the very low yield of kaonic Deuterium, a GEANT 4 MC optimization has been performed and three new detectors were added to the setup.
To account for exotic atoms production, for spin-to-spinless decay (F and r) and for machine background normalized input three new GEANT4 core classes were written.
The full DAFNE interaction region was included, to evaluate the effect of particle losses.

## Slide 22
SIDDHARTA-2 setup
k- detector
Veto-2
Veto-1

## Slide 23
SIDDHARTA-2 setup
384 SDDs
Target
Kaon Trigger
Veto-1
Veto-2
k- ID

## Slide 24
In conjunction with the top
scintillator of Ktrigger allows
fast degrader tuning
SIDDHARTA-2 Veto-1for kaon gas moderation
Improves S/B (and reduces the
contamination component)

## Slide 25
SIDDHARTA-2 Veto-1
Optics, contacts and segmentation
optimized by MC.

## Slide 26
SIDDHARTA-2 Veto-1

## Slide 27
SIDDHARTA-2 kaon charge identification
-Stopping both k+ and k- in a passive layer (teflon) and detect secondaries in a second one, thus avoiding the pileup on the tail of a high k pulse (tested with laser, low ID efficiency)
k-
p-
p
Fast prompt
83% crossing probability
k+
m+
k+
m+
Delayed prompt
53% crossing probability
5 mm scintillator
2 mm teflon
Geant4 cited sources:
C. Vander Velde-Wilquet, et al.,
- Determination of the Branching Fractions for K- Meson
Absorption at Rest in Carbon Nuclei, Nuovo Cim.
A 39 (1977) 538.
- K- -Meson Absorptions at Rest in Carbon Nuclei Leading
to Final States Containing a Lambda Hyperon, Nuovo Cim.
A 38 (1977) 178.
- The Conversion Probability and Emission Ratio of Charged
Sigma Hyperons Following K􀀀-Meson Capture at Rest in
Carbon, Nucl. Phys. A 241 (1975) 511.
Estimated k+ bkg rejection efficiency:
(0.83 * 0.5) + 0.5 ≈ 0.9
The k- ID on the bottom will enhance also the Veto1 k+ rejection, compensating inefficiencies, so granting >50%.

## Slide 28
SIDDHARTA-2 Veto-2 system
It consists in a set of scintillators read by SiPM,
placed under vacuum, behind each SDD array.
Correlation between SDD hadronic background and veto system response
Identifies grazing
MIPS from k-
absorption,
releasing an amount
of energy compatible
to an X-ray

## Slide 29
MC validation with SIDDHARTA 1 data
KH 106 pb
SIDDHARTA2
REAL DATA
KH 106 pb
SIDDHARTA1
MONTE CARLO
-The very same MC code (physics list, beam, materials) can
morph between SIDDHARTA and SIDDHARTA-2
-Despite the machine
background is a result of a
“cascade” of two different
MCs (DAFNE and SIDDHARTA),
the overall match (EM and
hadronic) is below 14%.

## Slide 30
A new set of SDDs with faster response time (500 ns FWHM vs 1 us in SIDDHARTA) and covering a larger area (246 cm2 vs 144 cm2 in SIDDHARTA) were designed and implemented, with the corresponding FE and DAQ.
SIDDHARTA-2 New SDDs
SDD drift time at 140 K

## Slide 31
S/B gain in SIDDHARTA-2 vs SIDDHARTA
Comment: all gain factors were set at minimum level. Several features depending on the
signal quality (gamma rejection, double anticoincidence, etc) were not included.

## Slide 32
De(1s) = 30 eV and DG(1s) = 70 eV
e.m.
Ka
Expected Kaonic Deuterium signal in SIDDHARTA-2

## Slide 33
SIDDHARTA-2 Kaonic deuterium measurement
First run, May – July 2023, integrated luminosity 200 pb-1 (with injections)
ROI
KN6->5 7595 eV
KC7->5 8886 eV
Cu K 8041 eV
KC5->4 10216 eV
KC6->5 5545 eV
KO7->6 6007 eV
PRELIMINARY
Next Steps:
Refined calibration
Veto-1 Veto-3
Injection selection
Fe 6400 eV
Data Analysis
strongly suppressed
in Run2

## Slide 34
SIDDHARTA-2 main results 2022-2023
The most precise KHe L-transition measurement in gas : J. Phys. G 49 (2022) 5, 055106
Kaonic helium-4 yields L-lines in gas : Nucl. Phys. A 1029 (2023) 122567
First measurement ever of intermediate mass kaonic atoms: Eur. Phys. J. A 59(2023)3, 56
First Measurement of KHe M-lines : paper submitted to J. Phys. G
First Measurement ever of kaonic Neon (record of precision < 1 eV) : analysis ongoing with implication on the possible charged kaon mass determination
First measurement of kaonic deuterium ( 200 pb-1 ) : DAQ and analysis ongoing

## Slide 35
SIDDHARTA-2 strategy
First run with SIDDHARTA-2 optimized setup for 200 pb-1 integrated luminosity: May – July 2023 - done
Second run Autumn – Winter 2023 (300 pb)
Third run: 2024 – 300 pb
Calibration runs: KHe; Neon; KH;…
Charged kaon mass exploring measurements:
-Runs with CdZnTe and HPGE in parallel with Kd
-Investigate diffractive techniques with crystal spectrometers with controlled mosaicity (VOXES)
Higher Z kaonic atoms transitions to fundamental level: new SDDs
1 mm thick produced, under test, to be installed at the end of kD run.
Possible development of a k+ low energy scattering setup

## Slide 36
"There is no exquisite beauty," says Bacon, Lord Verulam, speaking truly of all the forms and genera of beauty, “without some strangeness in the proportion."
Edgar Allan Poe

## Slide 37
SPARES

## Slide 41
M. A. Iliescu et al., "Reducing the MIPs Charge-Sharing Background in X-Ray Spectroscopic SDD
Arrays," in IEEE Transactions on Instrumentation and Measurement, vol. 70, pp. 1-7, 2021,
Art no. 9507807, doi: 10.1109/TIM.2021.3068149.

## Slide 42: Timing measurements at LNF-BTF

## Slide 43
Linearity of the new SDDs equipped with CUBE reset amplifier

## Slide 44
Linearity of the new SDDs equipped with CUBE reset amplifier
Range and calibration lines are very important: SIDDHARTA-2 cannot use so many lines due to kaonic atoms contamination.

## Slide 45
KHe 5->3 (M)
KHe 6->3 (M)
KHe 7->3 (M)
Ti K
Ti K
Line | Energy [eV]
K-4He M | 3300.8 13.2 (stat) 2.0 (sys)
K-4He M | 3860.4 13.6 (stat) 2.2 (sys)
K-4He M | 4214.1 19.6 (stat) 2.2 (sys)
Line | Energy [eV]
Kaonic 4He – M-series transitions (2022)
First observation and measurement of kaonic helium M-series transition New experimental data for cascade models calculations The X-ray yield is the key observable to understand the de-excitation mechanism in kaonic atoms and develop more accurate kaonic atoms cascade models.
Sgaramella F., et al, submitted to J. Phys. G Nucl. Part. Phys
45
SIDDHARTA-2
SIDDHARTINO
First measurement of K-4He M-series transition
Study of yield density dependence for the K-4He L transition

## Slide 46: First measurement of kaonic neon X-ray transitions
The Kaonic Neon measurement (2023)
K-Ne 8->7
K-Ne 7->6
KC 5->4
K-Ne 6->5
K-Ne 9->8
KAl 8->7
KAl 7->6 KC 6->4
KO 6->5
KO 5->4
KC 7->5
Line | Energy [eV]
K-Ne 98 | 4206.35 3.75 (stat)
K-Ne 8 | 6130.86 0.71 (stat) 2 (sys.)
K-Ne 7 | 9450.08 0.41 (stat) 2 (sys.)
K-Ne 6 | 15673.30 0.52 (stat) 5 (sys.)
Line | Energy [eV]
Implications on kaon - multinucleon interaction and kaon mass
First measurement of kaonic neon X-ray transitions ( record of precision eV )
Paper in preparation
46

## Slide 47
Kaon mass (K-Ne and K-Ne ) = (stat. error keV including the K-Ne )
The (charged) Kaon mass puzzle and kaonic Neon
Kaon mass discrepancy
The kaonic Neon measurement to determine the K- (K+) mass
Less systematic uncertainty with respect to DENISOV 91 and GALL 88 measurements, thanks to the use of a low Z gas (Ne) target
It could solve the kaon mass discrepancy issue
Particle Data Group, 2020, 083C01 (2020)
Impact on the charmonium spectrum and on all processes in which charged kaons are involved
DENISOV 91
GALL 88
SIDDHARTA-2
LUM 81
BARKOV 79
CHENG 75
BACKENSTO 73
Kaon mass [MeV]
Preliminary

## Slide 48
SDD energy calibration with ML and Differential Programming
Fabrizio Napolitano et al 2023 Meas. Sci. Technol. in press https://doi.org/10.1088/1361-6501/ad080a
The method can correct for miscalibration improving the systematic error and the energy resolution allowing to perform high precision measurement with an accuracy below 1 eV
Cu
Fabrizio Napolitano and Simone Manti

## Slide 50
Energy loss
PRELIMINARY
Preliminary evaluation with 2-body decay

## Slide 57
S0 p0 channel : the p0 momentum
mlim 12C at-rest
mlim 12C in-flight
At-rest
In-flight
In-flight component
P(p0) resolution: sp ≈ 12 MeV/c
P(p0) could be used for in-flight/at-rest separation
P(p0) (MeV/c)
M(S0p0) (MeV/c2)
Counts/(10MeV/c)
P(p0) (MeV/c)
M(S0p0) (MeV/c2)
Counts/(10MeV/c)

## Slide 59: Conclusions for AMADEUS
AMADEUS has a strong potential to perform complete measurements of low-energy kaon-nuclei interactions in various targets
Data analyses ongoing