## Slide 1: Development of thin GEM readout structures
Yasemin Schelhaas
MAGIX Collaboration Meeting 2017-02-16

## Slide 2: Topics
Layouts
  Manufacturing plans
Testing plans
Open questions

## Slide 3: Motivation
Aim: Small radiation thickness
Make material thinner
Material budget:
 Go to foil layout

## Slide 4: Traditional Layout
Problems:
Big and thick support structure
Crossed Cu strips
 Twice as much material as needed
 Go to one layer

## Slide 5: Strips & Pads design

## Slide 6: Strads design

## Slide 7: Layouts
Two different layouts:
  Strips (vertical) & Pads (horizontal)
  Strips of pads (vertical & horizontal)  “Strads“
Same pitch for both layouts: 400 µm to achieve 50 µm resolution
Pads as oblongs or octagons  increase field homogeneity
Connections of pads with tracks on the backside of the board
Panasonic connectors (AXK6SA3677YG, 130 pins)
Guard-Rings as a field shield
Designed in Cadence Allegro  Support from PRISMA Detector Lab

## Slide 8: Cadence Allegro Sketches
Strips & Pads
Strads

## Slide 9: Manufacturing plans
10 x 10 cm2 PCB prototype
  Test layouts
  Measure energy resolution
10 x 10 cm2 foil prototype
  Transfer layout to a thin foil
  Measure radiation thickness
30 x 30 cm2 PCB
  Enlarge first layout
  Measure resolution
  Observe electronics coupling
30 x 30 cm2 foil
  Final test of all parameters

## Slide 10: Testing plans
Test with a 55Fe source
  Measure energy resolution
  Stability
Test with cosmological radiation
  Homogeneity of detector and readout electronics
MAMI test-beam
  High rates
  Position resolution

## Slide 11: Open questions
Can all tests be done with existent GEM detector?
Do we need a new prototype?
Prototype where PCB can be changed easier, e.g. build in cover?
Make familiar with existent GEM detector?
Start preparing tests?

## Slide 12: Schedule & Outlook
Order PCB prototype boards until end of February
Test-beam: April 19-20
PRISMA support until October
End of master thesis: November 3, 2017